## Slide 1
Environmental physicochemical analysis of water, wastewater, soil and air
Learning objectives:
Upon completion of this chapter, the student should have knowledge of the following:
Describe water quality types
Explore water impurity and the need for quantification
Able to relate different units of measurement for water analysis Explain proper units and conversions in water, soil and air measurement.

## Slide 2: 1. Introduction
Substances introduced into the environment are distributed among the environmental compartments:
water (hydrosphere),
soil, rock (lithosphere), and
air (atmosphere), as well as among the organisms living on them (biosphere).
Only if we know the type and quantity of these contaminants can we protect the environment and its inhabitants.

## Slide 3: Water
Currently, ~ 900 million people suffer from drinking water shortages, circa 2.6 billion people live without safe sanitation and approximately 2.5 billion people have no wastewater treatment.
Five million people die every year as a result of deficient hygienic conditions, most of them children
About 1.5 million children die each year due to water-borne diseases
(UN 2010)
These issues particularly affect emerging and developing countries
As reported by Ethiopian demographics profile 2018
Drinking water source | Improved: Urban 93.1% , rural 48.6% and total 57.3% of population Unimproved: Urban 6.9%; Rural 51.4% and total 42.7% of population

## Slide 4
As its physical state changes, water passes through all spheres.
It is the most frequently analyzed environmental compartment and is also the easiest, because – unlike air or soil – it already exists in the liquid phase.
If drinking water samples are to be analyzed, sample preparation is usually not necessary; however, it is usually unavoidable in the case of wastewater samples.
Water (Cont’d)

## Slide 5: Water (Cont’d)
Parameter (Surface water) | Limit
BOD5 | < 5 mg/l O2
Chloride | 250 mg/l Cl
Chlorine, Residual | 5 μg/l as HOCl
Chromium | 50 μg/l Cr
Conductivity | 1000 μS/Cm (@ 20 °C)
Dissolved oxygen | minimum 6 mg/l O2
Fluoride | 1.0 mg/l F
Nitrate | 50 mg/l NO3

## Slide 6: Sustainable Development Goals: Targets related to WASH
3.3 by 2030 end the epidemics of AIDS, tuberculosis, malaria, and neglected tropical diseases and combat hepatitis, water-borne diseases, and other communicable diseases.
3.9 by 2030 substantially reduce the number of deaths and illnesses from hazardous chemicals and air, water, and soil pollution and contamination.
6.1 by 2030 achieve universal and equitable access to safe and affordable
drinking water for all.
6.2 by 2030 achieve access to adequate and equitable sanitation and hygiene for all, and end open defecation, paying special attention to the needs of women and girls and those in vulnerable situations.
6.a by 2030 expand international cooperation and capacity-building support to developing countries in water and sanitation related activities and programmes, including water harvesting, desalination, water efficiency, wastewater treatment, recycling and reuse technologies.
6.b support and strengthen the participation of local communities for improving
water and sanitation management.

## Slide 7: Challenges
Financing and budgeting process
  Insufficient financing
  Generating revenue through tariffs
  insufficient funding for operation and maintenance
Water governance
Deficient institutional and administrative structures, lack of political will, accountability and lack of stakeholder engagement
Water safety
Ensuring safe drinking water in the home is difficult

## Slide 8: Soil
multiphase
The soil is a hydrosphere, atmosphere,
lithosphere,
system in which the
and
biosphere
exist side by side.
It serves as a source of water and nutrients for plants, is a habitat for a large number of organisms, and is an important carbon sink.
Harmful soil pollutants can easily enter the human body through plants and animals.
The constituents of soil are very difficult to access and difficult to mobilize. Sample preparation usually involves extraction and digestion procedures.

## Slide 9: Soil (Cont’d)
Parameter | (mg/kg dry weight)
Chromium, total | 500
Chromium (VI) | 20
Lead | 40
Cadmium | 0.5
Mercury | 1
Nickel | 30
The soil forms the key basis of life for plants, animals, and humans.
Harmful substances contained in it come mainly from weathering, cultivation, or the air.

## Slide 10
Air
The atmosphere is an important thermal buffer against space, and protects the earth from cosmic radiation.
It is the place where clouds are formed and water is present there in all its physical states.
Thus it is a heterogeneous mixture of finely dispersed, solid or liquid particles in a gas (air). Its constituents are characterized by extreme mobility, enter our organism easily through breathing, and influence the climate and weather.
Filter methods, and aerosol and gas collectors bring the constituents of air into the aqueous phase, which is preferable for chemical analysis.

## Slide 11: Air (Cont’d)
Parameter | Standard [μg/m3] | Average time
SO2 | 500 | 10 minutes
 | 125 | 24 hrs
 | 50 | 1 year
NO2 | 200 | 1 hr
 | 40 | 1 year
CO | 100000 | 15 minutes
 | 60000 | 30 minutes
 | 10000 | 8 hrs
 | 120 | 8 hrs
PM10 | 50 | 1 year
 | 150 | 24 hrs
PM2.5 | 15 | 1 year
 | 65 | 24 hrs
Lead | 0.5 | 1 year
On average about 300,000
m3
air pass through a
person’s respiratory system in the course of a lifetime.
In this way, impurities in the atmosphere directly enter the lungs.
Especially dangerous are the aerosols that contain particles with diameters of less than 10 μm – also know as particulate matter.

## Slide 12: 1.1. General Facts
Currently there are a growing desire to restore and protect the env’t from degrading effects of all forms of pollution: air, water, soil, and noise
Three major questions usually arise when a particular type of pollution has been identified:
How serious is the pollution?
Is there standard procedure for sampling water, air and soil?
Is possible to quantify pollutants? &
This course is basically focuses on demonstration of laboratory equipment and apparatus, sampling, preservation, analysis and interpretation of the results.

## Slide 13
1.2. DEFINING ENVIRONMENTAL WATER QUALITY
WQ means d/t things to d/t people, depending on their goals for the water.
The env’tal health student express high-quality water as water in a pristine env’nt free from diseases causing pathogens and chemical sb/ces.
1.2.1 WATER-USE CLASSIFICATIONS AND WATER QUALITY STANDARDS
In human history, rivers, lakes, springs, & wells from which one can directly drink could readily meet almost all needs for high quality water.

## Slide 14: Cont’d
But now the water that is used for drinking water supplies, irrigation, and industry, …, needs treatment to become acceptable.
High-quality water is not pure; it just contains amounts of impurities too small to be harmful to its intended uses.
Many impurities in water are beneficial:
  carbonate (CO3-2) and bicarbonate (HCO3- )
  hardness and alkalinity
  dissolved CO2, and O2
Outside a chemical laboratory, extremely pure water generally is not desirable
What is water impurity?

## Slide 15: Cont’d
It is any sub/ce in water that is not derived from a water molecule only: harmful, beneficial, or neutral
A water pollutant or contaminant is any substance in water that is to be harmful to the water’s intended uses.
There are three d/t types of water quality standards set by U.S. state & federal regulations but there is only effluent & drinking water regulations in Ethiopia:
Surface and groundwater standards
Effluent standards
Drinking water standards

## Slide 16: 1.3. SOURCES OF WATER IMPURITIES
Natural sources
Human caused
Impurities can be divided into three classes:
regulated impurities (pollutants) considered harmful or aesthetically objectionable
unregulated impurities not considered harmful, and
unregulated impurities not yet evaluated for their potential health risks.

## Slide 17: 1.4. WHAT IMPURITIES ARE PRESENT?
The chemical content of a water sample is found by qualitative chemical analysis
Qualitative analysis identifies the chemical species present
WORKING WITH CONCENTRATIONS
Unfortunately, there is not one all-purpose method for expressing concentration
The best choice of concentration units depends in part on the medium (liquid, solid, or gas), and in part on the purpose of the measurement

## Slide 18
WORKING WITH CONCENTRATIONS (Cont’d)
In water samples, impurity concentrations are typically reported as:
milligrams (mg)
micrograms (µg), or
nanograms (ng) of impurity per liter (L) of water sample.
1 mg/L = 10-3 g/L = 1 part per million (ppm)
1 µg/L=10-6 g/L = 1 part per billion (ppb)
1 ng/L = 10-9 g/L = 1 part per trillion (ppt)

## Slide 19: WORKING WITH CONCENTRATIONS (Cont’d)
In soil samples, impurity concentrations are typically reported as milligrams, micrograms, or nanograms of impurity per kilogram of soil sample
1 mg/kg = 10-3 g/kg = 1 part per million (ppm)
1 µg/kg = 10-6 g/kg = 1 part per billion (ppb)
1 ng/kg = 10-9 g/kg = 1 part per trillion (ppt)
In gas samples (normally air samples), concentrations cannot be expressed as simply as in water or soils, because gas volumes and densities are strongly dependent on temperature and pressure.

## Slide 20: Unit of measurement for air analysis
Concentrations of air pollutants are commonly expressed as the mass of pollutant per unit volume of air mixture, as mg/m3, g/m3, ng /m3
1ppm= 0.0001 % by volume.
The relationship between ppm and mg/m3 depends on the gas density, which in turn depends on:
  Temperature
  Pressure
  Molecular weight of the pollutant

## Slide 21: Unit of measurement for air analysis (cont’d)
The ff expression can be used to convert the units b/n ppm and mg/m3 at any temp. or pressure.
mg/m3 = 273 x ppm x molecular wt. x pressure/22.4 x temperature
Example 1: Federal standard limits hourly carbon dioxide levels to
0.8 ppm. Express this concentration in terms of g/m3 at 270C and 1 atmospheric pressure.
Solution
Molecular weight of carbondixide = 12+16 +16 = 44;
Temperature = 27 +273 = 300K
mg/m3 = 273 x 0.8 ppm x 44 x 1 atm./22.4 x 300K; = 1.43
=>1430 g/m3