## Slide 1: Taguchi Method for DOE

## Slide 2: Introduction
Taguchi methods of experimental design provide a simple, efficient and systematic approach for the optimization of critical parameters of any process.
It is an effective method in investigating the effects of multiple factors on performance as well as to study the influence of individual factors to determine which factor has more influence, which less.
It minimizes to a great extent, the number of experiments by means of incorporating readily available fractional factorial matrices or orthogonal arrays.
Taguchi experiment can be accomplished within a limited time frame and at a reduced cost, with results comparable to that of a full factorial experiment

## Slide 3: Taguchi’s Design Stages
Taguchi recommends a three-stage process to achieve desirable product quality by design :
  System Design
  Parameter Design
  Tolerance Design.

## Slide 4: Parameter Design
The objective of the parameter design is to optimize the settings of the process parameter values for improving performance characteristics.
Optimal process parameter values are insensitive to the variation of environmental conditions and other noise factors. (Robust Design)
Parameter design is the key step in the Taguchi method to achieving high quality without increasing cost.
Orthogonal arrays, variance and signal to noise analysis are the essential tools of parameter design.

## Slide 21: Example
Experimental variable and their levels | Level 1 | Level 2 | Level 3
Spindle speed(rpm) | 250 | 355 | 500
Feed rate(mm/rev) | 0.18 | 0.24 | 0.32
Depth of cut(mm) | 0.5 | 1 | 1.5
Please use Taguchi’s L9 array for this experimental table

## Slide 22: Taguchi DOE is a Robust design
Robust design is an engineering methodology for obtaining product and process conditions, which are insensitive to various noise to produce high-quality products with low development and manufacturing costs.
Taguchi’s parameter design is an important tool for robust design.

## Slide 23: Insensitivity to Noise
Noise = Factors which the engineer can not or chooses not to control
  Unit-to-unit
    Manufacturing variations
  Aging
    Corrosion
    UV degradation
    wear
  Environmental
    human interface
    temperature
    humidity

## Slide 24: Taguchi DOE
Dr. Taguchi’s approach has two important areas.
First, he clearly defined a set of Orthogonal Arrays (OAs), each of which can be used for many experimental situations.
Second, he devised a standard method for analysis of the results.
The combination of standard experimental design techniques and analysis methods in the Taguchi approach produces a higher degree of consistency and reproducibility of the predicted performance.

## Slide 25: Orthogonal Arrays(OAs)
For designing experiments, Taguchi utilized a special set of tables, called orthogonal arrays (OAs), which represent the smallest fractional factorial experiments
The use of these arrays helps determine the least number of experiments needed for a given set of factors thus reducing the time and cost of experimentation.

## Slide 26: Types of OA
There are three types of OAs,
  OAs for two-level factors,
  OAs for three-level factors
  OAs for four-level factors
  OAs for mixed-level factors.

## Slide 27: Taguchi Designs