## Slide 1
McVeagh P and Brand Miller J (1997) Human milk oligo- saccharides: only the breast. Journal of Paediatric Child Health 33: 281-286.
Picciano MF (2001) Representative values for constituents
of human milk. Pediatric Clinics of North America 48: 53-67 (appendix 263-264).
Rodriguez-Palmero M, Koletzko B, Kunz C and Jensen R (1999) Nutritional and biochemical properties of
human milk. 2. Lipids, micronutrients, and bioactive factors. Clinics in Perinatology 26: 335-359.
Rudloff S and Kunz C (1997) Protein and nonprotein nitrogen components in human milk, bovine milk, and
infant formula: quantitative and qualitative aspects in infant nutrition. Journal of Pediatric Gastroenterology and Nutrition 24: 328-344.
HYGIENE IN DAIRY PRODUCTION AND PROCESSING
D J Reinemann, University of Wisconsin, Madison, WI, USA
Copyright 2002, Elsevier Science Ltd. All Rights Reserved
Introduction
This article presents an overview of the principles of hygiene for dairy production and processing equipment. The types of soils encountered in milk- handling equipment, elements of cleaning and sani- tation processes and types of cleaners and sanitizers are described. A description of hygienic procedures used for on-farm equipment is presented in a separate article (see Milking and Handling of Raw Milk: Milking Hygiene). This section emphasizes hygiene in dairy plants and presents a detailed discussion of hygiene processes and the composition of cleaning and sanitizing agents.
Hygiene Principles
Hygienic conditions are essential in milk-handling equipment to avoid loss of product quality and as- sociated reduction in shelf-life as well as to protect public safety. The food product should be free of levels of bacteria that could affect the product and that could cause foodborne illness. Dairy foods should also be free of adulteration from cleaning compounds. Quality control of the cleaning and sanitation processes should be part of the Hazard Analysis and Critical Control Point (HACCP)
programme in dairy plants (see Hazard Analysis and Critical Control Points: Processing Plants).
A hygiene programme begins with the design of the milk-handling systems and equipment to ensure that the product is not contaminated during handling and that the handling equipment can be easily cleaned and sanitized. Effectiveness in both the cleaning and sanitizing processes are necessary. Residual deposits must be such that bacteria are deprived of sites for attachment and multiplication.
Hygienic principles for milk-handling equipment are similar for milk production facilities on diary farms and milk-processing facilities in dairy plants. In general, dairy plants use more sophisticated systems due to the complexity of the flow circuits and larger scale of equipment. Dairy plants typically use clean- in-place (CIP) systems, in which cleaning and sanitizing compounds are circulated through the milk- handling equipment (pipes, storage tanks, process containers, heat exchangers, etc.). A CIP system per- forms the cleaning and sanitation functions without the need for disassembling the milk-handling equip- ment. There are, however, typically some compo- nents in both dairy plants and dairy farms that must be disassembled and cleaned manually or by some other means.
In ultra-high temperature (UHT) processes a con- tinuous feed of sterile product must be applied to an aseptic packaging line. The requirement for sterile conditions in both processing and packaging equipment makes hygiene in UHT plants especially challenging. Mineral and protein deposition is ac- celerated in heat-exchange equipment using UHT
1360 HYGIENE IN DAIRY PRODUCTION AND PROCESSING

## Slide 2
processes, further increasing the challenges of clean- ing and sanitizing. Heat exchange surfaces also present cleaning difficulties because it is difficult to achieve high flow velocity and the resultant vigorous mechanical cleaning forces. Improved chemicals and cleaning regimes for high-temperature process equipment have been one of the most active areas of research on cleaning in the past 10 years.
Water is the ma1or constituent of almost all cleaning and sanitizing compounds. The presence of suspended solids, minerals or other dissolved con- stituents can have a significant influence on the effi- cacy of cleaning and sanitizing agents. Chemical concentrations can be increased to account for some components in water, such as mild 'hardness'. It may be more economical to treat the water used for cleaning and sanitation rather than to compensate by adding more chemicals. In some cases, water treat- ment to remove specific components, such as iron and silicates, may be the only option in order to achieve adequate cleaning and sanitation. Water with less than 60 mg l-1 of hardness components is considered soft, 60-120 mg l-1 moderately hard, 120-180 mg l-1 hard, and above 180 mg l-1 very hard.
CIP systems rely on the combination of chemical, thermal and mechanical actions for cleaning and sanitation. A cleaning/sanitizing failure can result from a failure of any of these three components. Chemical action is provided by the constituents of the cleaning and sanitizing solutions. Thermal energy is provided by heating the cleaning or sanitizing solutions before circulation. Heat can also be added through heat exchangers in the cleaning flow circuit. Mechanical energy is produced by the turbulent flow of solutions through pipes and equipment with a relatively small cross-section. In components with a large cross-section and/or volume, mechanical action is produced by spraying solutions onto prod- uct contact surfaces. It is generally more difficult to maintain surface temperatures in spraying opera- tions than in pipe flow conditions. It is common to increase chemical concentrations in situations where mechanical or thermal energy is limited.
A cleaning/sanitizing process is typically made up of the following components, some of which may be combined into a single step and some of which may contain several steps:
1. Residual product and large debris is removed by allowing components to drain and discarding the collected material. This process may be facilitated by passing compressed air or air under vacuum through system components. It is essential that all components of dairy-processing equipment are installed so that they will drain.
A prerinse is applied to reduce organic soil load by eliminating any remaining residual product and other easily soluble or suspendable deposits. The prerinse may also be warmed to transfer heat to soil layers and equipment and begin wetting and loosening adhered soils to facilitate sub- sequent operations.
A cleaning compound is applied to remove remaining organic deposits. Detergents reduce the surface tension of water so that the solution can more effectively wet and penetrate soils adhering to surfaces and facilitate subsequent removal. Various components of detergents act to displace adhered soils from surfaces by saponi- fication of fats, peptizing proteins and dissolving minerals.
An acid wash may be applied to dissolve mineral deposits.
A final rinse is applied to carry away soils suspended during the cleaning step and to remove residual cleaning solutions.
A sanitizer is applied to kill any remaining
bacteria. The sanitation step may be performed immediately after cleaning if the equipment will be used again immediately, or prior to the next use of the milk-handling equipment if there is any substantial idle time.
The normal cleaning frequency in dairy plants is once per day, corresponding with breaks in the normal processing schedule. This interval may be longer in piping and components that are used con- tinuously. On dairy farms, milking machines must be cleaned more often, usually at least twice and often three times per day, corresponding with the milking frequency of the herd. More frequent cleaning is re- quired for milking machines, even if used continu- ously, because of the increased bacterial load resulting from handling a nonpasteurized product that can have a significant bacterial load.
There has been increased interest recently in optim- izing cleaning and sanitizing systems in order to reduce energy consumption and minimize other environmental impacts. These overall goals can be aided by ensuring that the mechanical cleaning forces are used to their greatest advantage. Optimization of mechanical cleaning actions will result in reduced chemical and water usage. A detailed knowledge of the type of soils and water composition of the indi- vidual dairy plant will result in optimal chemical formulations both to ensure a hygienic plant and to avoid overuse of chemicals. An added benefit to optimizing chemical concentrations is reduced wear and degradation of process equipment. There has also been continued research to develop cleaning
HYGIENE IN DAIRY PRODUCTION AND PROCESSING 1361

## Slide 3
and sanitizing agents that pose fewer environmental concerns than the traditionally used caustics and chlorine-based compounds.
It has become common to capture and reuse cleaning solutions in dairy plants. This practice results in considerable savings of energy as well as significant reduction in chemical use and discharge to the environment. Several attempts have been made to employ chemical recycling systems on dairy farms, but this practice has not become widespread because of the increased complexity, additional management requirements and marginal economics of recycle systems on small farms.
Regulations
There are a variety of regulations and laws specifying the minimum requirements for dairy hygiene in general and for equipment construction and opera- tions specifically. While there is a trend towards harmonization of these rules and regulations, they are still quite different in different countries. Knowledge of these regulations is essential to design a hygiene programme that meets the needs of its location. Most regulatory schemes include some type of requirement for the bacteriological safety of the final product. Specific requirements may be applied to specific organisms. Regulatory structures have also tended to include specific requirements for the construction and materials used in various types of equipment. This strategy can limit the adoption of new techno- logical developments, which are occurring at an ever-increasing rate. The increasing use of HACCP monitoring in dairy and other food-processing plants is a world-wide trend. Newer regulatory schemes, which may include HACCP monitoring programmes, tend to place increasing emphasis on quality and safety outcomes rather than specifications of equip- ment. This approach has become more practical as sensing technology and automated monitoring and control systems have become more sophisticated and more widely used.
Milk Soils and Deposits
Milk-handling and processing results in soils con- sisting primarily of minerals, lipids (fats), carbo- hydrates (sugars) and proteins. Other potential contaminants in milk-handling equipment include dust, microorganisms, lubricants, and cleaning and sanitizing componds.
Proteins are insoluble in water, slightly soluble in acidic solutions and highly soluble in alkali solutions. Proteins are one of the more difficult deposits to remove, especially if they have been denatured.
Mineral deposits develop slowly on unheated sur- faces and are typically white or grey in appearance. Waterstone formation results from precipitation of calcium and magnesium when sodium carbonates are added to hard water. Calcium phosphates in milk may adhere to surfaces forming 'milkstone'. This process is accelerated at high temperatures because calcium phosphates become less soluble. Another form of milkstone is protein that is denatured and deposited on heated surfaces. Milkstone is usually a porous deposit, which can harbour microbes, while waterstone is relatively inert.
Minerals are generally removed with acidic com- pounds; however, the cleaning regime depends on the type and intensity of the deposit. Acid washes are strong solutions designed to remove accumulated mineral deposits while acid rinses are milder solutions designed to prevent the build-up of mineral deposits. In general, freshly deposited soils of all kinds are easier to remove than deposits that have accumulated over time.
Lipid (fat) deposits are water insoluble and hence must be removed by a combination of thermal and chemical means. The first rinse of the cleaning process is generally performed at a temperature above the melting point of butterfat to remove the gross material left behind after milk-handling. A cleaning cycle using an alkali solution is then per-
formed to remove any fats still adhering to surfaces. Fats that come into contact with hot surfaces can
undergo polymerization, which increases the dif- ficulty of removal.
Sugars that have been deposited at low temperature are water soluble and generally easy to remove in the rinsing and cleaning cycles. When sugars come into contact with heated surfaces they may form a caramelized deposit that is difficult to removal.
The build-up of a soil/bacteria matrix, or bio-
film, on milk-handling equipment can protect bac- teria from the sanitizing process. These bacterial colonies can subsequently detach and contaminate the milk product. Porous or rough deposits are a more favourable surface for bacterial attachment. Biofilms have been observed to form on buna-N gasket material and in the crevices surrounding polytetrafluoroethene (PTFE) gaskets in dairy- processing lines but are less likely to form on smooth glass and stainless-steel surfaces. Biofilm formation begins with the deposition of a substratum, such as fibronectin, which increases surface tension and facilitates bacterial attachment. Deposition con- tinues as bacteria come into contact with and adhere to the surface and begin to produce attaching organelles. Adherence is further enhanced by the formation of polysaccharide capsules, flagellae and
1362 HYGIENE IN DAIRY PRODUCTION AND PROCESSING

## Slide 4
fimbriae. Cells bound in this structure have greater resistance to antimicrobials. The electrical charge of a surface and the pH and ionic strength of solutions affect the ability of biofilms to form. However, the main strategy for eliminating bio- films is to prevent their formation through proper cleaning.
Cleaning Agents
The solutions used to clean dairy production and processing equipment are generally complex mixtures of chemicals formulated to remove specific soils or combinations of soils deposited on specific materials. The ma1or function of cleaning ingredients is to reduce the surface tension of water so that soils deposited on surfaces can be loosened and removed. The following list of terms describes various cleaning processes and constituents of cleaners:
Anionic possessing a negative electrical charge.
Buffer a chemical that causes a solution to resist pH change when acid or alkali is added.
Cationic possessing a positive electrical charge.
Chelation a process in which an organic compound is added to water to prevent water hardness constituents and salts of calcium and magnesium from depositing on equipment surfaces by binding these salts to their molecular structure. Chelating agents can also bind other ions.
Deflocculating the action of breaking up aggregates
or 'flocs' into smaller individual particles.
Detergent any substance that, either alone or in a mixture, reduces the thermal of mechanical work requirements of a cleaning process.
Emulsification the physical breakdown of fats and oils into small droplets that are then dispersed in
solution. The soil is still present, but because of its reduced physical size will remain suspended in
solution for a longer period of time.
Hydrophilic having an affinity for or capability of dissolving in water.
Hydrophobic being antagonistic to water, or incap- able of dissolving in water, and usually having an affinity for oils and fats.
Nonionic lacking an electrical charge. Nonionic wetting agents consist of a balance of negatively
(anionic) and positively charged (cationic) com- ponents, resulting in a net neutral state.
Peptization formation of a colloidal solution from partially soluble protein soils. Alkaline cleaners peptise proteins by breaking peptide bonds.
Rinse-ability the ability of a cleaning compound to
be easily removed from a surface with a minimal amount of residue.
Saponification the chemical reaction between an alkali and an insoluble animal or vegetable fat (i.e. long-chain fatty acids) to form a soluble crude form of soap (sodium or potassium salt of a long-chain fatty acid).
Sequestration holding ionic forms of e.g. calcium or magnesium in solution so that they cannot form precipitates or interfere with cleaning or rinsing. These unstable salts will break down in the presence of alkaline compounds or at a high temperature. Many alkaline cleaning com- pounds are more effective at an elevated tem-
perature; however, a high-temperature cleaning solution contributes to precipitation of calcium
and magnesium carbonates, commonly known as scale. A sequestrant is an inorganic chemical that allows alkaline compounds to operate at higher temperatures because it prevents ions from combining with the detergent and forming insoluble curds that could produce precipitated deposits.
Surfactant a complex molecule that reduces the
surface tension of water to permit closer contact between the soil deposit and cleaning medium.
Suspension a dispersion of particles in a liquid. The suspended particles may be solids or another liquid, such as a fat or oil.
Water hardness refers to the amount of salts, such as
calcium chloride, magnesium chloride, sulphates and bicarbonates, present in water. Hardness can cause mineral deposits and soap to curdle, thus increasing the amount of soap needed to be effective.
Permanent hardness refers to the amount of cal- cium and magnesium chlorides and sulphates in water. These salts are rather stable and soluble under most conditions, thus causing minimal problems with cleaning.
Temporary hardness, or bicarbonate hardness, refers to the amount of calcium and magnesium bicarbonates in water, which are relatively soluble but unstable. Their unstable condition contributes to white deposits on equipment, heat exchangers and water utensils.
Total hardness is the combination of permanent and temporary hardness.
Water softening the removal or inactivation of cal- cium, magnesium and other ions in water through sequestration, precipitation or ion exchange.
Wetting agent (surface-active agent) a substance that lowers the surface tension of water, thus increas- ing its ability to contact surfaces. This is caused by the resultant action of a surfactant that, due to its
HYGIENE IN DAIRY PRODUCTION AND PROCESSING 1363

## Slide 5
chemical structure, is capable of wetting or penetrating the soil deposit to start the loosening process from the surface.
Cleaners are generally classified as either acidic or alkali compounds. The primary function of acidic compounds is to dissolve inorganic (mineral) deposits while alkali compounds are used primarily to dissolve organic deposits (fat and protein). The alkalis used in cleaning compounds include:
sodium hydroxide or caustic soda (NaOH)
sodium carbonate (Na2CO3)
sodium bicarbonate (NaHCO3)
sodium sesquicarbonate (Na2CO3 · NaHCO3
· 2H2O)
sodium tetraborate or borax (Na2B4O7 · 10H2O)
sodium metasilicate (Na2SiO3 · 5H2O)
sodium orthosilicate (2Na2O · SiO3 · 5H2O)
sodium sesquisilicate (3Na2O · 2SiO2 · 11H2O)
trisodium phosphate or TSP (Na3PO4 · 12H2O)
tetrasodium pyrophosphate, TSPP (Na4P2O7).
The following inorganic (also called mineral of strong acids) are commonly used for cleaning:
hydrochloric acid (HCl)
sulphuric acid (H2SO4)
nitric acid (HNO3)
phosphoric acid (H3PO4).
The organic (or weak) acids are generally not as corrosive to metals and are less irritating to skin than inorganic acids. They include:
acetic acid
hydroxyacetic acid
lactic acid
gluconic acid
citric acid
tartaric acid
laevulinic acid.
A variety of other constituents are added to amplify the acid/alkali removal processes and to protect equipment surfaces from cleaning compound. Chlorine is often added to alkaline detergents as a peptizing agent to aid in protein removal and to improve the rinse-ability of the detergent. The activity of cleaning solutions generally increases with increasing temperature and chemical concentration. Excessive temperature can, however, cause volatil- ization of some chemical constituents, thus reducing their effectiveness or causing proteins to denature and accelerate mineral deposition.
Wetting agents contain both hydrophobic and hydrophilic elements and thus have affinity for both
oils and water. Anionic wetting agents are pH neut- ral and are usually compatible with acid or alkaline cleaners, but on with cationic wetting agents such as quaternary ammonia compounds. Nonionic wet- ting agents are more effective on oils than anionic agents and only marginally affected by water hard- ness. Nonionic wetting agents are compatible with either anionic or cationic agents and some also suppress foam.
Considerable work has been done on the develop- ment of enzymes as cleaners or additives to conven- tional cleaning solutions. Enzyme cleaners have had limited success for use on specific processing equip- ment but have not yet been widely adopted in the dairy industry. A critical factor in the success of enzyme cleaners appears to be matching the specific enzyme to the specific type of soil. This can be a limitation when soils are composed of a wide variety of substances. Enzyme cleaners must also operate in a narrow temperature and pH range to avoid deactivation, which can also be a limitation in many cleaning situations.
Sanitation Agents
Sanitizing, as it is commonly understood when applied to dairy-processing equipment, is the reduc- tion of microorganisms to acceptably low numbers. Sanitizing differs from sterilization, which implies the destruction of all microbial life. Sanitizers are applied to surfaces that have already been cleaned in order to kill microorganisms that have survived the cleaning and/or equipment storage process. Residual soil deposits reduce the effectiveness of sanitation by providing incubation sites for microorganisms and protecting microorganisms from sanitizing agents. Residual organic matter can also react with chemical sanitizers and reduce the concentration of their ef- fective ingredients. The most common forms of sanitizing used in dairy plants are steam, hot water and chemicals. Milk-handling equipment used on dairy farms is generally sanitized using chemical sani- tizers. Chemical sanitizers are commonly circulated through milk-handling equipment using the CIP cir- cuit. The most commonly used chemical sanitizers are chlorine compounds, iodophors and acid sanitizers.
Steam Sanitizing
Steam sanitizing is accomplished by maintaining stem in contact with product constant surfaces for a designated time (typically 15 min contact with
condensate temperature above 80 oC). The dis-
advantages of steam as a sanitizer are: high energy
1364 HYGIENE IN DAIRY PRODUCTION AND PROCESSING

## Slide 6
cost, the danger of human contact with steam, and the difficulties of distributing steam evenly and thor- oughly to all contact surfaces.
Hot-Water Sanitizing
Hot-water sanitizing is accomplished by pumping heated water through equipment, usually using the same circulation equipment as for cleaning solutions. Typical contact times are in the range of 5 min with a minimum outlet temperature of 80 oC. The disadvantage of hot-water sanitizing is the high cost of energy to heat the water.
Chlorine Sanitizers
The range of microorganisms killed by chlorine- based sanitizers is probably broader than that of any other approved sanitizer. Bacteria, viruses, moulds, yeasts, spores, algae and protozoans are all inhibited to some degree. Chlorine-based sanitizers are used as surface sanitizers at concentrations of 100-200 mg kg-1 of available chlorine.
When liquid chlorine (Cl2) and hypochlorites are mixed with water, they hydrolyse to form hypo- chlorous acid (HOCl). Free residual chlorine is a measure of the portion of the total chlorine content that is in the form of hypochlorous acid and which therefore will react readily. Chlorine com- pounds are most effective as antimicrobial agent
at lower pH, where the presence of hypochlorous acid is dominant. Hypochlorous acid dissociates in
water to form hydrogen ions (H+) and hypochlorite ions (OCl-).
Chlorine may react or bind with elements in water. Breakpoint chlorination is the point at which the chlorine demand of water has been satis- fied. The free residual chlorine increases in nearly
direct proportion to the amount of chlorine added beyond the breakpoint. Total residual chlorine is
the amount of chlorine in all forms remaining in water after the chlorine demand has been met. Chlorine compounds can be generated at the point of use by electrolysis of sodium chloride brine (nascent chlorine).
The most active and widely used chlorine com-
pounds are hypochlorites of calcium (CaOCl) and sodium (NaOCl). Chlorine sanitizers are effective against Gram-positive and Gram-negative bacteria and conditionally against certain viruses and spores. Active chlorine reacts with, and is inactivated by, residual organic matter. Bromine has been used alone or in combination with other compounds as a sanitizer. The addition of bromine to a chlorine compound can increase the effectiveness of both bromine and chlorine.
Chlorine is easily volatilized during storage, especially if stored improperly, or during mixing of the product prior to use, especially if solutions are mixed at high temperature. Chlorine volatilization can cause significant reduction in the available chlorine in products and/or sanitizing solutions.
Iodophor Sanitizers
Within iodine-based sanitizers, iodophors receive the most extensive use in the food industry. Water- soluble iodophors are formed when elemental iodine is complexed with nonionic surface-active agents or carriers. Combining iodophors with surface-active agents and acids results in a solution with detergent properties and qualifies them as detergent-sanitizers. Iodophors have greater bactericidal activity under acidic conditions and are often modified with phos- phoric acid.
Iodine is as effective in the deactivating of ve- getative cells but not as effective as chlorine in spore inactivation. Iodine sanitizers are more effect- ive than other sanitizers on viruses. Iodine sanitizers are somewhat more stable in the presence of organic matter than chlorine compounds; however milk and other organic material will still cause inactivation of the iodine in iodophor solutions.
The amount of free available iodine determines the activity of iodophors. Iodophors are more costly than chlorine-bases sanitizers and are normally used at much lower concentrations (12-25 mg l-1). A potable water rinse is required if the iodophor concentration exceeds 25 mg l-1. Iodine compounds can be used at very low concentrations (6-25 mg l-1) at low pH. Use of iodophors in highly alkaline water can severely impair their efficacy if acidity is neutralized. For- mulated iodophors have a long shelf-life; however, iodine in solution is lost by vaporization. Vaporiza- tion of iodine is especially rapid when solution tem- peratures exceed 50 oC. Iodine can be absorbed by plastic materials and rubber gaskets, with resultant staining and antiseptic tainting. Acidic iodophors will prevent mineral build-up if used regularly but are not generally effective to remove heavy mineral deposits.
Acid Sanitizers
Acid sanitizers are considered toxicologically safe, and rinsing and sanitizing steps can be combined when using acid sanitizers. Organic acids, such as acetic, lactic, proprionic and formic acids, are used most frequently. Acid sanitizers neutralize alkalinity from detergents and prevent the formation of alkaline deposits on sanitized surfaces. The efficacy of acid sanitizers on individual organisms is dose-dependent.
HYGIENE IN DAIRY PRODUCTION AND PROCESSING 1365

## Slide 7
Acid sanitizers are most effective on stainless-steel surfaces or where contact time may be extended.
Acid-anionic surfactants are mixtures of an acid, usually phosphoric, with and anionic detergent. The range of bacteria killed by acid anionic surfactants includes vegetative cells of both Gram-negative and Gram-positive species; however, bacterial and fungal spores are resistant.
The advantages of acid sanitizers are that they are heat stable up to 100 oC and are relatively unaffected by the presence of organic matter. They are effective over a broad range of vegetative cells and are com- patible with most food-handling equipment surfaces. The disadvantages of acid sanitizers are high cost and corrosiveness to iron and some other materials.
Quaternary Ammonium Sanitizers
Quaternary ammonium compounds or 'quats' are synthesized when tertiary amines are reacted with halides. They have strong wetting properties and adsorb readily to inert surfaces and to the surfaces of microorganisms. The greatest effectiveness of quats is on Gram-positive bacteria, whereas Gram-negative organisms may not be appreciably affected. The antifungal properties are quite variable and fungal spores are relatively resistant to quats.
One of the problems associate with quats is their ability to support growth of resistant micro- organisms, principally pseudomonads; however, other genera have also been found to develop resistance. Quats are strongly cationic in solution and are incompatible with anionic detergents.
Oxidant Sanitizers
An oxidant sanitizer is created when acetic acid and hydrogen peroxide are combined to form peroxy- acetic acid. This mixture is normally diluted from a concentrate and used only after surfaces are thor- oughly cleaned. Surfaces must be thoroughly rinsed after treatment to avoid corrosion. The concentrated solution must be handled carefully and temperatures greater than 40 oC may cause loss of activity.
Ozone has been used extensively as an oxidizing sanitizer for drinking water but has found limited application as a surface sanitizer. Ozone is desirable in situations where chlorinated byproducts could be problematic. Ozone is usually generated onsite as a gas using a high voltage electric arc. The con- centrated gas is extremely volatile and harmful if inhaled.
See also: Biofilm Formation. Dairy Plant Effluent: Design and Operation of Dairy Effluent Treatment Plants. Flow Equipment: Principles of Pump and Piping Calculations; Pumps; Valves. Hazard Analysis and Critical Control Points: Processing Plants. Heat Exchangers. Milking and Handling of Raw Milk: Milking Hygiene; Effects of Storage and Transport on Milk Quality. Milking Machines: Principles and Design. Process and Plant Design. Ultra-High Temperature Treatment (UHT): Aseptic Packaging.
Further Reading
Austin JW and Bergeron G (1995) Development of bacterial biofilms in dairy processing lines. Journal of Dairy Research 62(3): 509-519.
Katsuyama AM (ed.) (1993) Principles of Food Processing Sanitation, 2nd edn. Washington, DC: The Food Processors Institute.
Marriott NG (1989) Principles of Food Sanitation.
New York: Van Nostrand Reinhold.
Neavesa P (1995) UHT plant cleaning: problems and
solutions. International Biodeterioration and Bio- degradation 36(3-4): 461-462.
Smith KE and Bradley RL (1987) Evaluation of efficacy of
four commercial enzyme-based cleaners of ultrafiltra- tion systems. Journal of Dairy Science 70(6): 1168- 1177.
Tra ga0 rdha G and Johanssona D (1998) Purification of alkaline cleaning solutions from the dairy industry using membrane separation technology. Desalination 119(1-3): 21-29.
Troller JA (1993) Sanitation in Food Processing, 2nd edn.
London: Academic Press.
1366 HYGIENE IN DAIRY PRODUCTION AND PROCESSING