## Slide 1: Chapter 4
Frame Relay

## Slide 2: Introduction
Packet-Switching Networks
  Switching Technique
  Routing
  X.25
Frame Relay Networks
  Architecture
  User Data Transfer
  Call Control

## Slide 3: Packet-Switching Networks
Basic technology the same as in the 1970s
One of the few effective technologies for long distance data communications
Frame relay and ATM are variants of packet-switching
Advantages:
  flexibility, resource sharing, robust, responsive
Disadvantages:
  Time delays in distributed network, overhead penalties
  Need for routing and congestion control

## Slide 4: Circuit-Switching
Long-haul telecom network designed for voice
Network resources dedicated to one call
Shortcomings when used for data:
  Inefficient (high idle time)
  Constant data rate

## Slide 5: Packet-Switching
Data transmitted in short blocks, or packets
Packet length < 1000 octets
Each packet contains user data plus control info (routing)
Store and forward

## Slide 6: Figure 4.1 The Use of Packets

## Slide 7: Figure 4.2 Packet Switching: Datagram Approach

## Slide 8: Advantages over Circuit-Switching
Greater line efficiency (many packets can go over shared link)
Data rate conversions
Non-blocking under heavy traffic (but increased delays)

## Slide 9: Disadvantages relative to Circuit-Switching
Packets incur additional delay with every node they pass through
Jitter: variation in packet delay
Data overhead in every packet for routing information, etc
Processing overhead for every packet at every node traversed

## Slide 10: Figure 4.3 Simple Switching Network

## Slide 11: Switching Technique
Large messages broken up into smaller packets
Datagram
  Each packet sent independently of the others
  No call setup
  More reliable (can route around failed nodes or congestion)
Virtual circuit
  Fixed route established before any packets sent
  No need for routing decision for each packet at each node

## Slide 12: Figure 4.4 Packet Switching: Virtual-Circuit Approach

## Slide 13: X.25
3 levels
Physical level (X.21)
Link level (LAPB, a subset of HDLC)
Packet level (provides virtual circuit service)

## Slide 14: Figure 4.5 The Use of Virtual Circuits

## Slide 15: Figure 4.6 User Data and X.25 Protocol Control Information

## Slide 16: Frame Relay Networks
Designed to eliminate much of the overhead in X.25
Call control signaling on separate logical connection from user data
Multiplexing/switching of logical connections at layer 2 (not layer 3)
No hop-by-hop flow control and error control
Throughput an order of magnitude higher than X.25

## Slide 17: Figure 4.7 Comparison of X.25 and Frame Relay Protocol Stacks

## Slide 18: Figure 4.8 Virtual Circuits and Frame Relay Virtual Connections

## Slide 19: Frame Relay Architecture
X.25 has 3 layers: physical, link, network
Frame Relay has 2 layers: physical and data link (or LAPF)
LAPF core: minimal data link control
  Preservation of order for frames
  Small probability of frame loss
LAPF control: additional data link or network layer end-to-end functions

## Slide 20: LAPF Core
Frame delimiting, alignment and transparency
Frame multiplexing/demultiplexing
Inspection of frame for length constraints
Detection of transmission errors
Congestion control

## Slide 21: Figure 4.9 LAPF-core Formats

## Slide 22: User Data Transfer
No control field, which is normally used for:
  Identify frame type (data or control)
  Sequence numbers
Implication:
  Connection setup/teardown carried on separate channel
  Cannot do flow and error control

## Slide 23: Frame Relay Call Control
Frame Relay Call Control
Data transfer involves:
  Establish logical connection and DLCI
  Exchange data frames
  Release logical connection

## Slide 24: Frame Relay Call Control
4 message types needed
SETUP
CONNECT
RELEASE
RELEASE COMPLETE