## Slide 1: Laser scanning and 3D Point Clouds

## Slide 2: The concept
Notes: 2

## Slide 3: Light Detection And Ranging
Device that automatically collects 3D co-ordinates at a high rate
Terrestrial Laser Scanning (TLS) = Technique that uses LiDAR (Light Detecting and Ranging) measurement technology. TLS consists of scanning with a LASER beam from the surface of the earth
Like taking a photograph with depth information
Each measured point has range and intensity values determined by the laser pulse properties plus an X, Y, Z value determined by the scanner’s orientation.
LiDAR is often used to refer to airborne laser scanning but can also apply to some ground based systems.

## Slide 4: What is LASER
A laser is a device that emits light through a process of optical amplification based on the stimulated emission of electromagnetic radiation.
The term "laser" originated as an acronym for "light amplification by stimulated emission of radiation”

## Slide 5: Principles of laser scanning
The electromagnetic spectrum
X-ray
Microwave
Mobile phones
Radio, Television
Human eye

## Slide 6: How laser works

## Slide 7: Principles of laser scanning
Laser light:
High degree of spatial coherence
 propagates dominantly in a well defined direction
 moderate beam divergence
High degree of temporal coherence
 large propagation distances
Narrow spectral bandwidth
 pure colour, e.g. red, green or blue
Linearly polarized
 oscillates in a particular spatial direction.
Travel with a finite and constant velocity in a certain medium
Highly suited for the measurement of objects

## Slide 8: What is laser scanning ?

## Slide 9: What is laser scanning ?

## Slide 10: What is laser scanning ?
Total Station  point based
Laser Scanner  surface based
The laser scanner are not pointable measuring devices unlike Total station. It measures
range in uniform increments of arc.

## Slide 11: Types of laser scanning
Static
Dynamic
Aerial
Manned aircraft
Drones
Terrestrial
Mobile mapping

## Slide 12: Types of laser scanning
Static
Dynamic
Aerial
Manned aircraft
UAV
Terrestrial
Mobile mapping

## Slide 13: Types of laser scanning
Field of view
Range
  Close range sub mm 100 pt/sec
  Mid range mm 1000-500000 pt/sec
  Long range centimeter > 500000 pt/sec
Accuracy
Speed
(150-1000m)
(1-150m)
(0.5-2m)

## Slide 14
Categories of laser range finding

## Slide 15: Categories of laser range finding
Triangulation scanner
γ
β
α
a
b
c

## Slide 16: Laser pulse-based, time based
Time of flight (TOF)
Since C=300 mm/ns (speed of light), 1mm range resolution requires 6.7 ps time
interval measurement resolution
n the refractive index of atmopshere

## Slide 17: Time of flight: Pulse characteristics
Time of flight can be 6.7 microseconds
Survey height of 1km.
=Pulse length

## Slide 18: Laser pulse-based, time based
Pulse laser scanners are reflectorless systems.
The energy of the reflected pulse depends on both physical factors : electric permittivity, magnetic permeability and conductivity
This depends on wavelength of the laser.
The time of flight is derived once the return Pulse amplitude crosses an internally defined threshold.

## Slide 19: Phase measurement techniques
Emitted light is amplitude-modulated with a constant frequency, f, sinusoid
Much higher measurement rates: several 100 kHz (pulsed: several kHz)
The measured phase shift between the emitted and received signal, Δφ, is used to calculate the time of flight
where n is the integer number of full wavelengths
The range is

## Slide 20: Phase measurement techniques
0
Amplitude
90
180
270
360
90
(a)
(b)
D
D
The technique is ambiguous
Notes: The phase shift is the change occurs in the phase or in the phase difference between two. A signal is transmitted by the total station and reflected by lens. As shown in the figure, the two way distance can be expressed as this equation. The fractional cycle can be computed by the difference of phase.

## Slide 21: TLS Selection and Classification
  According to the range measurement principle
  Triangulation: up to a few m range, accuracy < mm level
  Phase: up to 100 m, ~mm level accuracy
  Pulse (TOF), up to several 100 m, ~cm level accuracy

## Slide 22: Principle of Laser scanning
Four raw observables observable
Range
Angular measurements (Horizontal direction and Vertical angle)
Intensity (properties of the reflected signal) of the reflected laser signal
Time, to see the evolution of the measurements
Cartesian coordinates (X,Y,Z) are the quantities provided as output from most
scanners and are usually treated as observables.

## Slide 23: 3D Point Cloud
Cartesian transformation of the laser pulse data transformation of the range and reflectance images as (well as the calculated XYZ coordinates) in scanner centred reference frame
3D point cloud of discrete locations derived from
superimposing range and reflectance image for each
laser Pulse
3D point clouds are the basis for subsequent analysis and used to create CAD or GIS models

## Slide 24: Point clouds with intensity
The intensity is a measure of the electronic signal strength obtained by converting and amplifying the backscattered optical power.

## Slide 25: TLS Geometry
are coordinates of object point I In scan j
(Sensor frame)
(external system)

## Slide 26: TLS observations
The basic observation equations are
  Range
  Horizontal direction
  Elevation angle (Zenith angle)

## Slide 27: Observations (continued)

## Slide 28
Registration of 3D Point Clouds from Multiple scans

## Slide 29: Registration and Georeferencing in TLS
To obtain a complete representation of the scanned object, the point clouds (scans) should be first transformed to a common coordinate system. This procedure is called registration, whereby the registered scans are combined in one dataset
Large/complex objects needs to be scanned at multiple setups. However, the scanner measures the point clouds with reference to internally defined sensor frame
In order to be able to integrate the TLS data into other geospatial data [e.g. digital maps or DTM], the user has to transform the “registered” point cloud of the whole object into a chosen external (geodetic) coordinate system, which is either local or national. This procedure is called georeferencing

## Slide 30: Multiple scan poistions
Scan position 1
Scan position 2

## Slide 31: Registration
are coordinates of object point I In scan j
(Sensor frame)
(external system)

## Slide 32: Registration : Indirect registration
  3D space resection problem
  6 unknowns per point cloud
  6 co-ordinates from 3 non-collinear points needed for unique solution
  Most often formulated in terms of Cartesian scanner co-ordinates, i.e.,
In Spherical
Coordinates

## Slide 33: Registration (Continued)
Parametric least-squares used to estimate the 6 transformation parameters
Transformation of scanned points into object space is thus given by
Strictly speaking, the problem is best formulated in terms of observed spherical co-ordinates, i.e.

## Slide 34: Registration of multiple scans
The figure shows two scans of the object from two different positions.
In order to transform the Scan 2 into the CS of the Scan 1, determine the
transformation parameters between these two coordinate systems.
3 translations along the 3
coordinate axes: ΔX, ΔY, ΔZ;
3 rotations around the 3
coordinate axes: ω, φ , κ.

## Slide 35: Target based registration
scan 1
scan 2
T3
T1
T2
T1
T2
T3
Scan 1 and scan2
registered
Overlap
scan 1
scan 2
T3
T1
T2
Tie-points
Determine the targets centres to which the coordinates, used in the
registration, are referred.
Scan the targets with high resolution, so-called fine scans, with higher than the resolution of the main scan.
It should be a highly reflective target.
Target type

## Slide 36: Surface Matching
This approach assumes matching together the overlapping areas of the point clouds instead of matching just the common targets or natural point features. Since the overlapping areas contain typically thousands of points, the redundancy involved may lead to a better solution than using discrete tie-points alone
The figure shows how surface matching works

## Slide 37: Benefits of laser scanning
Non contact measurement
High accuracy
Long range
Speed
Safety
Accessibility of the object
Quantity of information
5 dimensional information
  X, Y, Z
  Intensity
  time

## Slide 38: Important issues
Scanner output = point cloud

## Slide 39: Important issues
Resolution ≠ Accuracy
Resolution
The average distance between XYZ co-ordinates in a point cloud
5x5mm
10x10mm
20x20mm

## Slide 40: Metrological Aspects: Errors
Instrumental
Propagation of laser beam
Mixed edge problem
Range uncertainty
Angular uncertainty
Object-related
Environmental
Temperature
Atmosphere
Interfering radiation
Distortion from motion
Methodological errors

## Slide 41: Material Reflection

## Slide 42: Material Reflection
Marble surface
Black surface

## Slide 43: Reflection on Multiple Surfaces

## Slide 44: APPLICATIONS

## Slide 45: Applications
Heritage ( stability analysis for virtual tour ), reverse engineering, chemical industry, forensics, monitoring reclamations, etc.
Notes: 45

## Slide 46: Multipurpose use .
3D Laserscanning
Damage survey
civil
Archaeology &
heritage
Mining
Art
geology
Everyday survey
petrochemistry

## Slide 47
Area of Application .
Quality checking .

## Slide 48
3D Management of Facilities .
Area of Application .

## Slide 49
Preparing a shutdown .
Area of Application .

## Slide 50
Design & Constructability .
Area of Application .

## Slide 51
Collision material
Petrochemistry explosion
Forensic
Damage Survey .
Area of Application .
Notes: Aanrijding van een transportband door een vrachtwagen in beerse
Gat in een tank
Overstroming van een spaarbekken, monitoring, …
Auto ongevallen

## Slide 52
Re-Engineering .
Area of Application .

## Slide 53
Other Possibilities .
Clash Detection
Simulation
  Impact of explosion
  Evacuation routes
As Built plans
  Growing safety regulations
  Minimizing Engineering schedules
Pre-survey scan for new installations
...
Area of Application .

## Slide 54
Roads
Railways
Tunnels
Bridges
Buildings
Civil .
Area of Application .
Notes: Globe is using it’s laserscanner for many different purposes.

## Slide 55
Art & Nature .
Area of Application .
Notes: Aanrijding van een transportband door een vrachtwagen in beerse
Gat in een tank
Overstroming van een spaarbekken, monitoring, …
Auto ongevallen

## Slide 56: TLS applications
Landscape evolution
Fault mapping
Paleoseismology
Paleontology
Cryosphere
Ecology
Landslides
Volcanoes
Sediment transport
Stratigraphy
Coastal processes
Non-Earth sciences:
forensics, movies, games, architecture, archaeology, civil engineering, manufacturing, etc.
And many more …