## Slide 1: Part I – Water Supply
CHAPTER 2b
COMPONENTS OF WATER SUPPLY SYSTEMS
Institutional

## Slide 2: OUTLINE
INSTITUTIONAL
  MANAGEMENT PERSPECTIVE
  ASSET MANAGEMENT
  ENVIRONMENTAL MANAGEMENT

## Slide 3
WATER
(SUPPLY)
POPULATION
(DEMAND)
SOCIO-ECONOMY
(DEMAND)
ENVIRONMENT
(Availability / Climate / Pollution)
POLICY/ GOVERNANCE
(Design Standards /Operating rules and regulations)
SETTLEMENT
(Demand Centre)
WATER SUPPLY SYSTEM

## Slide 4: Institutional / Management Perspective/ Framework
Water Committees / Rural
Water Supply and Sanitation Offices /Boards
Water Boards / Municipalities
Municipal Utilities / AWSA …
Project Initiation / Implementation

## Slide 5: Asset Management
What is Asset Management?
Asset Inventory
Level of Service
Critical Assets
Life Cycle Costing
Long-term funding
Implementation

## Slide 6: What is Asset Management?
Water and Wastewater Systems are made up of assets (Visible /Buried)
  Physical components : pipe, valves, tanks, pumps, wells/ dams, hydrants, treatment facilities, ….
Water / Wastewater Assets generally lose value over time as the system ages and deterioriates
  Cost of OM increases as assets age
Asset management is an approach on managing the assets of the system that can assist the utility with making better decisions on managing aging assets

## Slide 7: What is Asset…?/ Goal
Goal of Asset Management
  The International Infrastructure Management Manual defines the goal of asset management as
    meeting a required level of service
      in the most cost -effective way through
        the creation, acquisition, operation, maintenance, rehabilitation, and disposal of assets
          to provide for present and future customers.

## Slide 8: What is Asset…?/ why care??
A community, water or wastewater utility should care about managing its assets in a cost effective manner:
  1) These types of assets represent a major public or private investment;
  2) Properly - run infrastructure is important in economic development;
  3) Proper operation and maintenance of a utility is essential for public health and safety;
  4) Utility assets provide an essential customer service; and
  5) asset management promotes efficiency and innovation in the operation of the system.

## Slide 9: What is Asset…?/ Objective
The intent of asset management is to ensure the long -term sustainability of the water or wastewater utility.
  By helping a utility manager make better decisions on
    when it is most appropriate to repair, replace, or rehabilitate particular assets and
      by developing a long-term funding strategy, the utility can ensure
        its ability to deliver the required level of service perpetually.

## Slide 10: What is Asset…?/ Benefit
The benefits of asset management include, but are not limited to, the following:
  Better operational decisions
  Improved emergency response
  Greater ability to plan and pay for future repairs and replacements
  Increased knowledge of the location of the assets
  Increased knowledge of what assets are critical to the utility and which ones aren’t
  More efficient operation
  Better communication with customers
  Rates based on sound operational information
  Increased acceptance of rates

## Slide 11: Core Components of Asset Management
Asset Inventory
Level of Service
Critical Assets
Life Cycle Costing
Long-term Funding Strategy

## Slide 12: Asset Inventory
What Do I Own?
Where Are My Assets?
What is the Condition of My Assets?
What is the Remaining Life of My Assets?
What is the Value of the Assets?
Organizing the Asset Inventory

## Slide 13: What Do I Own?
Determine who was operating, managing and/or owning the system at the time of the major construction periods (when a large number of assets were put in place.) Interview these individuals and gather as much information as possible regarding their recollections of what assets were installed and where they were installed. If there are maps of the system, these can be used during the discussions.
Examining any as-built or other engineering drawings of the system
Visual observations of above-ground or visible assets (e.g., hydrants, pumps, manholes, treatment works)
Interviewing community residents who may have lived in the area during construction and who are familiar with the construction activities (especially helpful in very small towns in which the residents were actively involved in developing the utility)
Estimates on buried assets using above ground assets as a guide (e.g., using manholes to estimate locations, size, and type of pipe between the manholes; using isolation valve loc ations to estimate buried water pipe locations)

## Slide 14: Where are My Assets
1) mapping the assets and
2) putting a location in the inventory.
  In terms of mapping, the most important factor is to have a visual picture of the asset locations, especially the buried assets.
  The map can be as simple (hand drawn) or as complex (Geographic Information System) as the system is capable of.

## Slide 15: What is the Condition of My Assets?
A condition assessment can be completed in many different ways, depending on the capability and resources of the system.
The group can then select a condition ranking approach
  0 through 5,
  A through F,
  Excellent through unacceptable, etc.)
    and ask the group to look at the list of assets and rate each asset using the selected methodology.
This approach uses the best information available but does not require systems to gather additional data in order to rate the assets.

## Slide 16: What is the Remaining Life of My Assets?
All assets will eventually reach the end of their useful life. Some assets will reach this point sooner than other assets. In addition, depending on the type of asset, it will either reach that point through amount of use or length of service.
  For example, a pump will wear out sooner if it is used more and will last longer if it is used less. The actual age of the pump is not as important as the amount of work the pump has done.
  On the other hand, pipe assets wear out based more on the length of time in the ground. If a pipe is in the ground for decades it has had considerable time to contact the soil around it and the water within it and may start to corrode.

## Slide 17: …Life of Asset
As an example, if a given water utility routinely replaced its chlorinator every 5 years because that was as long as that asset lasted, then 5 years should be used as chlorinator life, not a standard default value.
However, if the system only had its pipe in the ground for 20 years and had no knowledge of how long it could be expected to last, it could use a standard default value of between 50 to 75 years.
However, as time goes on, if the system did not notice any reduction in the integrity of the pipe after 40 years, the useful life could be increased from 50 years to say 75 to 100 years.
If the system started seeing a reduction in the pipe integrity (lots of breaks due to corrosion) at 40 years, it would keep the useful life closer to 50.

## Slide 18: What is the Value of the Assets?
Generally, when utilities consider the value of assets, they think about the cost of initially installing the assets.
  This cost has no other importance than historical information or it can be used by a system that depreciates the costs of assets over time.
  However, the installation cost does not have a direct bearing on what it will cost to replace that asset when it has reached the end of its useful life.
    The asset may not be replaced by the same type of asset (e.g., cast iron pipe may be re placed by PVC pipe) or it may be replaced by a different technology entirely (e.g., a chlorination system replaced by an ultraviolet disinfection facility).
    Furthermore, costs of various assets may change drastically over time, such that the cost of installing pipe in 1956 in no way reflects the costs of installing pipe 50 years later in 2006.

## Slide 19: …Value of Asset
The real value of the assets is the cost it would be required to replace the assets using the technology the system would employ to replace them.
  If the system has asbestos cement pipe now, but would replace the system with PVC pipe, the real value of the assets is the cost of replacement using PVC and the installation cost associated with PVC.
Although the idea behind an asset value is relatively simple, obtaining costs for the asset replacement is not as easy. Small utilities may not have the expertise to estimate replacement costs.
  If the system has had recent improvements, such as pipe replacement, information regarding the cost per linear meter can be used.
  If a neighboring system that is similar has had work done, costs obtained in their project may be used.
  Organizations that complete a large number of construction projects per year may be able to provide estimates

## Slide 20: Organizing the Asset Inventory
There are many options regarding how to manage the asset inventory data. Specific options include:
  Commercially available software for asset inventory
    Most preferred as it easy to get required information but it could be expensive, requires highly trained manpower
  Generic database software
    Better option with regard to cost but not as flexible as commercially available software
  Spreadsheet software
    Cheap, time taking and cumbersome and difficult to get all required information (example: “Provide me a list of all pipes installed in 1950 that are cast iron that have had at least 1 break in the last 10 years.”
    “Provide me a list of all pipes installed in 1950 that are cast iron that have had at least 1 break in the last 10 years.”
  Hand written inventory
    Better than nothing but could not be used to manage asset in an efficient manner and is not flexible, updating is also difficult

## Slide 21: ….Asset Inventory
Example :
“Provide me a list of all pipes installed in 1950 that are cast iron that have had at least 1 break in the last 10 years.”
  This list can be obtained in a matter of moments with a database.
  However, with a handwritten list or a spreadsheet, answering a question like this would be an extremely tedious and time - consuming activity.

## Slide 22: … Asset Inventory / Mapping
Small Scale Mapping / 1:100,000 (wider area / overall view)
Large Scale Mapping / 1:25,000 (detail info / small area)
Mapping Source /Yahoo/Google/USGS/EMA…
Knowledge of GIS / Database necessary to include both location and data info

## Slide 23: Level of Service
A Level of Service Agreement (LOS) defines the way in which :
  the utility owners, managers, and operators want the system to perform over the long term.
The LOS can include any :
  technical,
  managerial, or
  financial components the system wishes,
    as long as all regulatory requirements are met.
The LOS will become a fundamental part of how the system is operated.

## Slide 24: Why a Level of Service Agreement?
There are two key facets to asset management –
  defining the level of service the system will strive to provide its customers over the long term and
  determining the most efficient and economical way to deliver that service (the least cost approach).
Therefore, determining and detailing the level of service that the system is going to provide is a key step in the overall process.

## Slide 25: …LOS Agreement
The Level of Service Agreement – the document that will spell out the service the system wishes to provide – is a multi-faceted tool that can fulfill a wide array of purposes :
  Communicate the system’s operation to the customers (residential, industrial, or commercial)
  Determine critical assets
  Provide a means of assessing overall system performance
  Provide a direct link between costs and service
  Serve as an internal guide for system management and operations staff
  Provide information for system annual report or annual meeting presentation
  Reduce system costs through customer involvement

## Slide 26: … LOS/Communication
Communicate to customers times of outage if some source stops or depleted / or shifting is required (if not dissatisfaction could occur)
  LOS Agreement can include
  “In the event of an outage, the system will move water around so that no area is without water for more than 1 day.
  The rotation of water movement will be posted in a public area so that customers know when they will be with and without water.”

## Slide 27: …LOS/ Critical Assets
The LOS can be one factor in determining critical assets.
  An example of how the LOS can impact criticality is where a system’s LOS includes the factor “water will be delivered to customers 99% of the time.”
  If the system has only one water source, the source will be a critical asset for the system.
  It must keep the source operational at all times in order to meet this criteria.

## Slide 28: …LOS/Assessing Overall System Performance
Agreed LOS
Breaks will be repaired within 6 hours of initiation of repair 95% of the time.
Customer complaints will be responded to within 24 hours, Monday through Friday.
Losses will be kept to less than 15% as measured by m3 pumped each month – m3 sold each month.
System will meet all state and federal regulations.
Performance
250 breaks occurred, 230 (92%) were fixed in less than 6 hours
30 complaints were received, all 30 responded to within 24 hours
Losses over the year as follows: January 12%, February 10%, March 19%, April 14%, May 9%, June 13%, July 9%, August 10%, September 12%, October 9%, November 10%, December 12%
System met all regulations; no violations

## Slide 29: …LOS/ System performance
Based on this data, the system met some, but not all of its LOS factors. The following items were met:
  The customer complaints were responded to on time and the system met all the state and federal regulations.
  The following items were not met: breaks were not repaired within 6 hours and the losses were not kept to less than 15% in all months.
The system can look at these results and determine the items that it needs to work harder on in order to meet the level of service requirements.

## Slide 30: Provide a Direct Link Between Costs and Service
There is a direct link between the Level of Service provided and the cost to the customer.
  When a higher LOS is provided, the costs to the customers will likely increase.
This relationship provides an opportunity for the water system to have an open dialogue with its customers regarding the LOS desired and the amount the customers are willing to pay for this level of service or increased services.
  For example, customers may complain about aesthetic contaminants in the water – those contaminants that cause taste, odor, or color issues in the water, but not health concerns – and wish to have these contaminants removed. The water system can install treatment to remove these contaminants but it will cost each customer more for their water each month.

## Slide 31: Serve as an Internal Guide to System Operation and Management
It is much easier to operate or manage a system when the operations and maintenance staff as well as the management staff understand the goals of the operation.
These goals allow the operations staff to have a better understanding of what is desired from them and the management has a better understanding of how to use staff and other resources more efficiently and effectively.
Checking how well the system is meeting LOS also allows the management to shift resources if need be from one task to another to meet all the goals more effectively.

## Slide 32: Provide Information for Annual Report or Meeting
If the system tracks information regarding how well it is meeting the LOS criteria on a weekly or monthly basis, it can use this information to prepare an annual report regarding how well the system met these criteria over the course of a year.
This information can be presented to the customers at an annual meeting so that customers are aware of how well the system met the overall goals for the operations of the system.
This meeting would also be an opportunity to discuss any changes needed in the LOS, based on the operations data.
Perhaps some of the LOS conditions are not possible to be met given the current staff or resources.
the system will either have to reduce the LOS provided or increase staff or other resources in order to meet the current LOS.
The decision to increase staff or other resources or decrease LOS will directly impact customers, so it is important to use the opportunity of the annual meeting to discuss the potential options with them.

## Slide 33: What is the minimum starting point?
Federal / Regional Law
Policies / Strategies / Regulations…
Accepted Local and/or International guides

## Slide 34: What else should be included in LOS?
The maximum level of the LOS is defined by the maximum capabilities of the assets.
A system cannot include something within a LOS that the system is not capable of doing.
if the system wishes to include the provision of fire flow in its LOS, but it only has 2 and 4 inch lines with no fire hydrants, there is no way the system can provide fire flow.
The system may wish to include the provision of fire flow in its long –range Capital Improvement Plan and seek funding for a system upgrade to provide this, but until the assets for fire flow are in place, fire flow provision should not be included in the LOS.
Within the range of the minimum (regulations) and maximum (capabilities of assets) there are numerous items a system could include within its LOS.

## Slide 35: Examples of items that can be included in the Level of Service
Number of breaks per km that are acceptable
Length of time from report of a leak or break until repair
Amount of notification (and method) prior to a scheduled shut down
Amount of notification (and method) prior to a non -scheduled but non-emergency shutdown
Quantity of unplanned interruptions in service verses planned interruptions
Number of hours to fix the pipe break once on site
System losses maintained at less than X% overall
Maximum system flow will be X m3/d
No detection of TC or EC at the source

## Slide 36: Examples of items that can be included in the Level of Service
Water pressure will be maintained throughout the system at X bar
Rates will be raised annually to avoid rate shock in the system
Rates will be reviewed annually
Storage capacity will be maintained at X m3 total
No water outage will be longer than X hours total
Customers will be notified of planned system outages at least X hours or X days before the interruption
Customers will be notified at least X minutes prior to shut down for an emergency condition, unless life threatening conditions cause a need for immediate shut down
Water conservation will be instituted to reduce average daily use by X percent in Y years
Note
The LOS does not have to be lengthy; it can concentrate on a few key items the system really wishes to focus on

## Slide 37: How can the public be involved in the LOS?
Ideally, the public or customers of the utility would be actively involved in the development of the LOS.
This involvement could be done through focus group meetings, surveys, public meetings, or other means.
In a practical sense, it is difficult to get the customers to attend meetings or complete surveys and it can be difficult for them to understand certain components of the LOS.
  For example, customers may not understand how many breaks per mile may be acceptable prior to pipe replacement.
Rather, the best-case scenario may be to ask for specific input on items that directly affect the customers and for which they would have a reasonable understanding of the social and economic costs associated with the item.

## Slide 38: Can the LOS be Changed Over Time?
Similar to the overall Asset Management Program that will change and adjust over time, the LOS may need to be adjusted from time to time. This adjustment may be required
  because the system may discover that it is too costly to operate the system at the levels previously defined.
  Or the adjustment may be necessary due to new rules or regulations that require a change.
  Additionally, the customers may feel that they desire a different level of service. For example, the system may not be providing fire flow to all customers. The customers may decide that they are willing to pay for the upgrades to the system to provide fire protection. In this case, the LOS may need to be revised to reflect the fact that “all customers are to receive fire protection

## Slide 39: Critical Assets
Not all assets are equally important to the system’s operation; some assets are highly critical to operations and others are not critical at all.
Furthermore, critical assets are completely system specific.
Certain assets or types of assets may be critical in one location but not critical in another.
  For example, one system may believe their chlorinator is a critical asset because they lack redundancy and have been known to have total coliform in their source.
  Another system may feel their chlorinator is not a critical asset because they have a redundant system and adequate spare parts to fix the broken chlorinator quickly.
A system must examine its own assets very carefully to determine which assets are critical and why?

## Slide 40: …Critical Assets / Determining
In determining criticality, two questions are important.
  The first is how likely the asset is to fail and
  the second is the consequence if the asset does fail.

## Slide 41: …Critical Assets / Causes of Failure
Likelihood of Failure
The data available to assist in this determination is:
  asset age,
  condition assessment,
  failure history,
  historical knowledge,
  experiences with that type of asset in general, and
  knowledge regarding how that type of asset is likely to fail.
Consequences of Failure
The costs include:
  cost of repair,
  social cost associated with the loss of the asset,
  repair/replacement costs related to collateral damage caused by the failure,
  legal costs related to additional damage caused by the failure,
  environmental costs created by the failure, and
  any other associated costs or asset losses.

## Slide 42: Critical… /Assessing
Assessing criticality requires an examination of the likelihood of failure and the consequence of failure as discussed above.
The assets that have the greatest likelihood of failure and the greatest consequences associated with the failure will be the assets that are the most critical.
The next most critical assets will fall into three main categories:
  Assets that have a very high likelihood of failure with low consequence
  Assets that have a very high consequence with a low likelihood
  Assets that have a medium likelihood and medium consequence
The remaining assets that have low consequence and low likelihood will be the least critical assets.

## Slide 43: …/Assessing
A technique such as a ranking table as presented below can be a good place to start in assessing criticality.

## Slide 45: …Criticality / Analysis over time
The condition of the asset will change over time as will the consequences related to failure.
  Costs of repair may go up, the community may grow, new roads may be built or similar factors may occur that cause the consequence of failure to change.
Therefore, it is necessary to periodically review the criticality analysis and make adjustments to account for changes in the likelihood of failure an d the consequence of failure.
The criticality analysis must be kept up to date to ensure that the utility is spending its time and resources on the appropriate assets
Also, the analysis must incorporate replacement of assets. If an asset that was critical primarily due to its likelihood of failure fails and is replaced with a new asset, the criticality number will go down since the likelihood of failure is much less.

## Slide 46: Life-Cycle Costing
This component is one of the most complex of all of the components of asset management.
Lifecycle Asset Management options and strategies considering all relevant economic focuses and physical consequences, from initial planning through to disposal. The Lifecycle components include:
  Asset Planning
  Asset Creation/Acquisition/Design
  Financial Management
  Asset Operation and Maintenance
  Asset Condition and Performance Monitoring
  Asset Rehabilitation/Renewal
  Asset Disposal
  Asset Audit and Review

## Slide 47: …Life-Cycle
There are four basic options for dealing with the actual assets over time:
  Operate and maintain the existing assets
  Repair the assets as they fail
  Rehabilitate the assets
  Replace the assets
These options are intimately connected to each other.
Choosing to do more or less of one impacts how much of the others is done, whether or not the other is done at all, or the time frame in which one of the others is done.

## Slide 48: …Life-Cycle
For example, choosing to spend more on operating and maintaining assets will decrease the need to repair the asset and will increase the amount of time until the asset is replaced.
Choosing to rehabilitate an asset will eliminate the need to replace the asset in the short term and will increase the amount of time until the asset ultimately needs to be replaced.
The rehabilitation will also reduce the amount of operation and maintenance that needs to be done and reduce the need for repairs.
The purpose of asset management is to try to determine the optimal way to spread the money between each of these categories, while maintaining the LOS desired.

## Slide 49: …Life-Cycle
Generally, the most expensive option is replacement of the assets.
Therefore, keeping the assets in service longer, while still meeting LOS conditions, will usually be the most economical for the utility over the long term.
The three other options: maintenance of the asset, repair of the asset, and rehabilitation are options that can be used to keep the asset in service longer.

## Slide 50: …Life-Cycle / Operation and Maintenance
Operation and maintenance (O&M) functions relate to the day -to-day running and upkeep of assets and are particularly relevant to short -lived dynamic assets (such as pumps) where deterioration through lack of regular maintenance may result in rapid failure.
O&M procedures can be categorized as operational, maintenance and (where applicable) laboratory.

## Slide 51: …Life-Cycle / OM
Operational procedures can be classified as:
  Standard Operating Procedure: most common, typically used during normal operations, day-to-day
  Alternate Operating Procedure: Used when operational conditions require that an asset or process be modified or taken off -line, scheduled, periodic
  Emergency Operating Procedure: used in emergency conditions, incorporated into overall emergency plan developed for facility
Maintenance procedures can be classified as:
  Corrective Maintenance Procedures: used by field technicians for the breakdown and repair of assets that are malfunctioning (e.g., replace broken bearing)
  Preventative Maintenance Procedures: developed to prevent breakdown and prolong asset life (lubrication or overhaul)
  Reliability-centered Maintenance Procedures: developed to assist maintenance managers in predicting asset failures and lessening effects on facilities (asset condition monitoring or failure modes and effects analyses)

## Slide 52: …Life-Cycle / OM
Laboratory procedures can be classified as:
  Equipment-related Procedures: developed on the basis of how to operate the equipment and what maintenance and/or calibration the equipment requires
  Sampling-related Procedures: developed around sampling routines and specify to the laboratory technician when, where, and how samples should be taken

## Slide 53: …Life-Cycle / OM Procedure Devt.
Several choices exist for who develops O&M procedures.
  New facilities or assets: engineering firm or designer, supply vendors, contract professional technical writer
  Existing facilities or assets: existing staff, technical writer
In order to develop O&M procedures the reference materials must be located. Reference materials include
  O&M Manuals,
  process and instrumentation drawings,
  vendor submittals,
  specifications,
  pictures,
  design data, design drawings, as -built drawings, and
  interviews with experienced staff.

## Slide 54: …Life-Cycle / OM Procedure Devt.
Developing operational procedure s includes:
  Titling the procedure appropriately, so it is easily identified. (e.g., “Shutdown of Alum Feeder Number 4”)
  Introduction: lists associated information such as the reason for the procedure, responsible parties, desired outcomes, safety procedures, special equipment requirements and notification requirements
  Steps and/or Activities: Step 1, Shut power off at the breaker located on the south wall labeled Alum Pump
  Note any cautions or hazardous conditions with each step or activity before the activity is performed

## Slide 55: …Life-Cycle / OM Procedure Devt.
The greatest reward for developing O&M procedures is that
  all operations activities, maintenance activities, and laboratory activities are backed by management and standardized across all shifts by all personnel.
  This ensures management consistency of personnel activities, product quality, and O&M costs.
  The application of standardized maintenance procedures can reduce asset downtime and ensure lifetime productivity.
  The application of standardized laboratory procedures is essential for a good quality - assurance/quality-control program.

## Slide 56: …Life-Cycle / OM Critical Assets
One of the purposes for identifying critical assets is to allow the utility to make more informed decisions regarding the use of its operation and maintenance dollars.
it is most advantageous to the utility to spend the greatest portion of its operation and maintenance budget on assets that are critical to the overall operation of the utility.
These assets have the greatest chance of costing the utility money if they fail.

## Slide 57: …Life-Cycle / Repair
In addition to operating and maintaining the assets, systems will need to plan for the repair of assets as they fail.
  Systems need to consider how long they will keep an asset in service prior to replacement of the asset. To some extent, these two items – repair and replacement - are off-setting.
  If more resources (personnel and money) are spent on repair, there will be a decreased need for replacement. On the other hand, if greater resources are applied to replacing the assets, fewer resources will be applied to repair.
  There is a balance between how much to spend in each category: maintenance, repair, and replacement to achieve the most efficient system.
(example – Car)
In comparing U.S. utilities to utilities in Australia and New Zealand,
  it has been observed that U.S. utilities generally replace assets much sooner than utilities in Australia and New Zealand who have fully implemented asset management.
  The asset management analysis these utilities have done, has shown them that it is generally more efficient to repair assets than to replace them.

## Slide 58: …Life-Cycle / Rehabilitation
When an asset fails, or approaches failure, the typical thought process is that of replacing the asset with a new asset.
There is another option for some water or wastewater system assets; assets may be rehabilitated rather than an outright replacement.
Rehabilitation brings the assets back to a useable condition without actually replacing them.
In many cases, it may be cheaper to rehabilitate the asset rather than replacing it, it may extend the life span of the asset considerably and may reduce other impacts related to asset replacement.
An example of a rehabilitation approach is slip lining a wastewater pipe that is nearing the end of its useful life. The pipe can be lined without having to dig the original pipe out of the ground, thus possibly reducing the costs of installation and the inconvenience of the construction.

## Slide 59: …Life-Cycle / Replacement
Asset will reach a point where it can no longer be kept in service through maintenance or repair or where the asset is no longer capable of meeting the LOS, either economically or at all.
  At that point, the asset will need to be replaced.
Replaced assets can either be
  part of a replacement schedule or
  a capital improvement plan.

## Slide 60: …Life-Cycle / Replacement
Replacement Schedule
  A replacement schedule should be developed that indicates those assets that will be replaced within the next 20 years that will be funded out of system revenues.
  the schedule will contain assets that are smaller dollar amount or routinely recurring and should include assets that will be paid for out of system revenues.
  A couple of examples of these types of assets are: water meters and chlorine pumps. Additional assets, such as small diameter water distribution piping, valves, and hydrants can also be included.
Repair and Replacement Schedule
  This schedule can also be expanded to include programmed maintenance or repair, making it a Repair and Replacement Schedule.
  The types of activities that can be included here are major, programmed repair elements, such as a storage tank inspection annually and a tank overhaul (repaint, structural testing, cleaning) or leak detection every 3 years.
  These are generally items that are annually or greater in schedule and that constitute a major budget expenditure.
  The Repair and Replacement Schedule should be updated annually so that it is always 20 years long.

## Slide 64: …Life-Cycle / Replacement
Capital Improvement Plan
  A long-term capital improvement plan should look at the utility’ s needs for the future. Ideally, the planning period would be at least 20 years, with a minimum of 5 years.
  Categories of Capital Improvement Plan

## Slide 65: …Life-Cycle / Replacement – Capital Improvement Plan
Capital Needs Related to Future/Upcoming Regulations
  The state and federal regulatory agencies periodically issue new rules and regulations that may require water or wastewater systems to invest in new technologies to meet the requirements. For example, when the arsenic standard was reduced from 50 parts per billion to 10 parts per billion, many water systems in New Mexico were required to consider capital needs to meet this standard.
  The capital needs may be related to treatment facilities, distribution system changes, connections with other sources, development of new sources, or any other type of capital project to meet the standard.
  Systems ought to be aware of upcoming regulations and consider the costs that may be associated with compliance so that money can be set aside to help pay the costs.

## Slide 66: …Life-Cycle / Replacement – Capital Improvement Plan
Capital Needs Related to System Expansion
  Over time, the system may expand due to growth in the area or through serving customers who were previously on private wells or septic tanks.
  This type of expansion may involve new distribution or collection pipes, additional storage, additional water source, or additional treatment.
Capital Needs Related to System Consolidation or Regionalization
  Some systems may find it advantageous to consolidate or regionalize with other nearby systems. In some cases, this type of regionalization may involve additional assets, such as sources, pipes, storage or treatment facilities.
Capital Needs Related to Improved Technology
  Systems may wish to replace assets because the technology of the assets originally installed is out of date and needs to be modernized or because technology improvements will allow improved customer service or enhanced efficiencies. An example of this type of capital needs is a SCADA system that electronically controls the system’s operations.

## Slide 67: …Life-Cycle / Replacement – Capital Improvement Plan
Capital Needs Related to Major Asset Replacement:
  Some assets can be repaired within the repair and replacement schedule, while others will be major expenditures that will have to be replaced under the capital improvements program.
  Assets such as storage tanks, treatment facilities, and major portions of the distribution or collection system could fall into this category.

## Slide 68: …Life-Cycle / Replacement – Capital Improvement Plan
System managers need to consider all of these types of needs when developing a long term Capital Improvement Plan or CIP. Each item needed by the system for each of the applicable categories for a 20 year time horizon needs to be identified. At a minimum, the following information should be identified for each item.
  Description of the project
  Brief statement regarding the need for the project
  Year project needed
  Is the year needed flexible or absolute
  Estimate of project cost
  How costs were estimated
  Funding source(s) considered/available for this type of project
  Changes in overall operations that may occur as a result of the project (include operator requirements, additional O&M costs, regulatory changes, any efficiencies that may be gained, etc.)
  Impact of the project on LOS

## Slide 73: Long-term Funding Strategy
The first four components of the asset management strategy lead a system to discover what actions are most appropriate to take to manage the system at the desired level of service at the lowest life cycle cost.
The final factor in the asset management strategy is determining the best manner in which to fund the operation and maintenance, repair, rehabilitation, and replacement of assets.
There are several sources of funding available to a system, so it is important to evaluate the item needing funding and the various options.

## Slide 74: Long-term Funding …
Funding Source Available
  The sources of funding for the overall operation and maintenance of a water or wastewater system, including asset repair, replacement, and rehabilitation include the following:
  System revenues from:
    User fees
    Hook up fees
    Stand-by fees
    Late fees
    Penalties
    Reconnect charges
    Developer impact fees

## Slide 75: Long-term Funding …
System reserve funds
Emergency reserves
Capital improvement reserves
Debt reserves
System generated replacement funds
Bonds
T axes

## Slide 76: Long-term Funding …
Non-System revenues:
State grants
State loans
Federal grants
Federal loans
State or federal loan/grant combinations

## Slide 77: Long term …Rates and Asset Management
System revenues are a major component of an asset management plan.
  The system revenues will fund the operation and maintenance of the system;
  there generally are no outside funding sources for routine operation and maintenance of a water or wastewater utility.
  In addition, the rates will need to fund reserve accounts for emergencies, repairs, and debt coverage (for any loans.)
A well developed rate structure will take into account needs for the water system for the current year as well as needs for the water system in future years, through reserve accounts.
  For example, if the water system is anticipating a new regulation that will require additional treatment, the system should be collecting money through the rates to help pay for the needed equipment.

## Slide 78: Long term …Rates and Asset Management
The rate structure should also anticipate
  routine replacements of parts, particularly those parts that wear out regularly.
  For example, if the system replaces its chlorinator every 5 years, the rates should cover this expense, rather than seeking state or federal funding to cover these types of needs.

## Slide 79: Long-Term Funding Strategy
The objective in preparing long -term financial forecasts is to outline the organization’s future financial requirements based on all information relating to asset creation, maintenance, renewal/rehabilitation and disposals.
  Three questions must be answered when preparing the strategy:
  What funds are needed to acquire, operate, maintain and renew the asset?
  When will the funds be required?
  How do these types of funds affect the utilities rates?
There are five types of expenditures that a utility needs to plan for. Each type of expenditure has a typical funding source associated with it as well.