## Slide 1: Part I Ch4 Alternative Water Supply Sources

## Slide 2: Alternative Water Supply Sources
Why alternative sources?
  Dwindling supply from traditional sources
  Development, operation and maintenance of centralized systems are expensive
Alternatives
  Rainwater harvesting
  Grey water reuse
  Desalination
  Cloud seeding

## Slide 3: Rainwater Harvesting

## Slide 5: Rainwater Harvesting
Rainwater can be used for non-potable purposes like toilet flushing, washing, etc
Contributes to the reduction of diffuse pollution

## Slide 6: Comparison of DRWH with other sources

## Slide 7: Elements of Rainwater Harvesting System
Rainfall Harvesting Potential (RHP)
RHP = Rainfall x Collector Area x Runoff coefficient
Amount runoff that can be supplied to the user U
U = Storage efficiency x RHP

## Slide 8: Collector-Roof characteristics
Type | Runoff coefficient | Notes
G I Sheets | > 0.9 | Excellent quality water. Surface is smooth and high temperatures help to sterilize bacteria.
Tile (glazed) | 0.6 – 0.9 | Good quality water. Unglazed can harbor moulds. Contamination can exist in tile joints.
Asbestos sheets | 0.8 – 0.9 | New sheets give good quality water. No evidence of carcinogenic effects by ingestion. Slightly porous so reduce runoff coefficient and older roofs harbor moulds and even moss.
Organic (Thatch) | 0.2 | Poor quality water Little first flush effect High turbidity due to dissolved organic material which does not settle.

## Slide 9: Conveyance- Gutter & downpipe
Water conveyance
Q = A v = A 1/n R^2/3 S^1/2
Interception
Gutter type
a) Plastic b) Aluminum c) Steel
d) Wood & Bamboo e) Half Pipe f) flexible guttering

## Slide 10: Storages
Material
Precast concrete
Steel
Plastic
Ferro cement
Bricks
Shape
Sphere
Cylinder
Half sphere
Cube
Location
Above ground
Underground

## Slide 11
Chart: 
| Bathroom | Dishwashing | Taps | Washing clothes | WC | Gardening | Other uses
Average Daily per capita water demand | 21.5 | 7.7 | 18.5 | 24.6 | 18.5 | 4.6 | 4.6
Figure 5 Breakdown of average daily per capita water demand, Jemo I condominium site, Addis Ababa, 2015

## Slide 12
Chart: 
| January | February | March | April | May | June | July | Augest | September | October | November | December
Average Rainfall | 12.4 | 32 | 60.7 | 88.1 | 80.6 | 144.6 | 274.4 | 294.8 | 178.1 | 34.6 | 9.4 | 9.5

## Slide 13
Chart: 
| May | June | July | Augest | September | October
Consumption | 45295 | 40599 | 39540 | 39569 | 39669 | 37471
Demand | 124119.6 | 124146 | 124278 | 124449.6 | 124462.8 | 124476
Water consumption rate related to demand at Jemo I condominium site, Addis Ababa 2015

## Slide 14
Single Residential Building Considering All Demand

## Slide 15
Single Residential Building Considering Non-Potable Demand

## Slide 16
Chart: 
| Single building | All buildings | All buidings with 110l/c/d
ALL DEMAND | 0.1 | 0.1 | 0.06
NON POTABLE DEMAND | 0.36 | 0.36 | 0.216
TOTAL DEMAND | 1 | 1 | 1
Percentage of demand that can be addressed by the RWH at Jemo I condominium site, Jemo Addis Ababa, 2015

## Slide 17: How much water can be harvested?

## Slide 18: Grey water Reuse

## Slide 19: Sources of Grey water

## Slide 20: Characteristics of Greywater

## Slide 21: Water Reuse- Potential Applications

## Slide 22: Use of Rainwater and Grey water

## Slide 23: Treatment matrix for reclamation and reuse of wastewater

## Slide 24: Treatment matrix for reclamation and reuse of wastewater

## Slide 25: Desalination of Water with high TDS

## Slide 26: Desalination Technologies