## Slide 1
Chapter 7
Agitation and Aeration

## Slide 2
Outline
Introduction
The oxygen requirement of industrial fermentation
Oxygen supply
Determination of KLa value
Factors affecting KLa value in fermentation vessels
Scale up

## Slide 3
Stock Culture
Shake Flasks
Raw Materials
Sterilization
Air
Agitator
Recovery
Purification
Products
Seed fermenter
Medium Formulation
Typical Bioprocessing

## Slide 4
Oxygen transfer
Majority of fermentation processes are aerobic and therefore require the provision of oxygen.
If the stoichiometry of respiration is considered then the oxidation of glucose is represented by
C6H12O6 + 6 O2 6H2O+6CO2
180 g
192g
Thus 192 g of O2 is required for 180 g glucose
Notes: Also oxygen is required for product formation ex: for pencillin production 2.2 gms of oxygen is required for 1g pencillin formation

## Slide 5
Microorganisms take up the substrate/ nutrient from liquid
Hence both O2 and glucose have to be available in liquid
Solubility of oxygen in water is 1.26 mmol/l at 25oC or approx 8 mg/l
This will reduce further in the presence of salt or acid
This solubility is 6000 times lesser than the solubility of glucose

## Slide 6
Thus it is not possible to supply entire oxygen required for batch fermentation in one addition
Oxygen will be supplied continuously at the rate of demand by the microorganism.
Oxygen is consumed quickly in aerobic cultures. For actively respiring yeast with 109 cells /ml oxygen in liquid have to be replaced 12 times in minute to keep up the cellular demand.
Notes: O2 in the liquid is measured as Dissolved oxygen concentration

## Slide 7
Oxygen transfer
How satisfying oxygen demand?
•
–
–
Aeration and agitation
Productivity is often limited by oxygen availability
This chapter:
–
•
•
•
Oxygen requirements of industrial fermentations
Quantification of oxygen transfer (KLa values)
Factors affecting KLa values in fermentation
vessels
Notes: The oxygen demand of an industrial fermentation process is normally satisfied by aerating and agitating the fermentation broth. However, the productivity of many fermentations is limited by oxygen availability and, therefore, it is important to consider the factors which affect a fermenter's efficiency in supplying microbial cells with oxygen

## Slide 8
Aeration and Agitation
Aeration is to provide microorganism in submerged culture with sufficient oxygen for metabolic requirements.
Agitation ensures that a uniform suspension of microbial cells is achieved in a homogenous nutrient medium.

## Slide 9
Oxygen requirement
What is happening in fact?
- Not only respiration of glucose
- Also biomass and product formation
carbohydrates
hydrocarbons oxygen demand
The more reduced the carbon source, the greater is the oxygen demand !

## Slide 10
Oxygen requirement
What is happening in fact?
- Not only respiration of glucose
- Also biomass and product formation
A culture demand for oxygen is very much dependent
on the source of carbon in the medium

## Slide 11
Oxygen requirement
Up to now: Overall Demand
Now: effect of dissolved oxygen (DOC) concentration on
QO2
Specific oxygen uptake rate (mmoles of oxygen / g dry weight cells and per hour)
Notes: However, it is inadequate to base the provision of oxygen for a fermentation simply on an estimation of overall demand, because the metabolism of the culture is affected by the concentration of dissolved oxygen in the broth

## Slide 12
Oxygen requirement
Fig. 9.1 it may be seen that the specific oxygen uptake rate increases with increase in the dissolved oxygen concentration up to a certain point(referred to as CCrit) above which no further increase in oxygen uptake rate occurs.

## Slide 13
oxygen requirement
Notes: Thus, maximum biomass production may be achieved by satisfying the organism's maximum specific oxygen demand by maintaining the dissolved oxygen concentration greater than the critical level.

## Slide 14
OXYGEN
REQUIREMENTS
•
•
Max
QO2
gives
max biomass production
DOC <
Ccrit:
– Biomass production may be disturbed
– Product formation may
or
•
DOC >
Ccrit:
– Biomass production not influenced
– Product formation may
Notes: Thus, maximum biomass production may be achieved by satisfying the organism's maximum specific oxygen demand by maintaining the dissolved oxygen concentration greater than the critical level

## Slide 15
Oxygen Requirements
Investigating the amino acid biosynthesis by Brevibacterium flavum provides an excellent
example of the effects of the dissolved oxygen concentration on the production of a range of
closely related metabolites
Oxygen excess should give rise to abundant TCA cycle intermediates, whereas oxygen
limitation should result in less glucose being oxidized via the TCA cycle, allowing more
intermediates to be available for phenylalanine, valine and leucine biosynthesis. Thus, some
degree of metabolic disruption results in greater production of pyruvate derived amino acids.
Notes: - members of the glutamate and aspartate families of amino acids was affected detrimentally by levels of oxygen satisfaction below 1.0
- whereas optimum production of phenylalanine, valine and leucine occurred at oxygen satisfaction levels of 0.55, 0.60 and 0.85, respectively

## Slide 16
OXYGEN SUPPLY
•
•
Cheapest available source: AIR
Laboratory-scale fermentors: shake-flask technique
Notes: The method for provision of a culture with a supply of air varies with the scale of the process:

## Slide 17
OXYGEN SUPPLY
•
•
Cheapest available source: AIR
Pilot and industrial fermentors: stirred aerated vessels

## Slide 18
OXYGEN SUPPLY
•
Transfer
of
oxygen
from air
bubble
to cell
air bubble
O2
O2
O
aerobic
micro-organism
2
1.
2.
3.
Transfer
Transfer
from bubble into medium
through medium
Uptake of dissolved oxygen by cell
Notes: The transfer of oxygen from air to the cell, during a fermentation, is occurring in a number of steps:

## Slide 19
OXYGEN SUPPLY
•
Transfer
of
oxygen
from air
bubble
to cell
air bubble
O2
O2
O
aerobic
micro-organism
2
1.
2.
3.
Transfer
Transfer
from bubble into medium
through medium
Uptake of dissolved oxygen by cell
rate limiting
step

## Slide 20
OXYGEN SUPPLY
•
Transfer of
oxygen from air bubble
to
cell
Notes: The rate of oxygen transfer from air bubble to the liquid phase may be described by the equation

## Slide 21
It is extremely difficult to measure both KL and 'a' in a fermentation and, therefore, the two terms are generally combined in the term KLa, the volumetric mass-transfer coefficient, the units of which are reciprocal time (h-1).
KL may be considered as the sum of the reciprocals of the resistances to the transfer of oxygen from gas to liquid and (C* - CL) may be considered as the 'driving force' across the resistances
The larger the KLa, the higher the aeration capacity of the system.

## Slide 22
The KLa value will depend upon the design and operating conditions of the fermenter and will be affected by such variables as:
- aeration rate,
- agitation rate and
- impeller design.
These variables affect 'KL' by reducing the resistances to transfer and affect 'a' by changing the number, size and residence time of air bubbles.

## Slide 23
OXYGEN SUPPLY
•
Transfer of
oxygen from air bubble
to
cell

## Slide 24
DETERMINATION of KLa VALUES
A number of different methods are available
Determination of KLa in a fermenter is important to establish its aeration efficiency and quantify effects of operating variables on oxygen supply.
It is important to remember that dissolved oxygen is usually monitored using a dissolved oxygen electrode which records dissolved oxygen activity or dissolved oxygen tension (DOT) while the equations describing oxygen transfer are based on dissolved oxygen concentration(DOC).
Thus, to translate DOT into concentration the solubility of oxygen in the fermentation medium must be known.
Notes: The solubility of oxygen is affected by dissolved solutes so that pure water and a fermentation medium saturated with oxygen would have different dissolved oxygen concentrations yet have the same DOT, i.e. an oxygen electrode would record 100% for both. Thus, to translate DOT into concentration the solubility of oxygen in the fermentation medium must be known and this can present difficulties.

## Slide 25
The sulphite oxidation technique
Gassing-out (static) techniques
Dynamic method of gassing out
DETERMINATION of KLa VALUES

## Slide 26
Dynamic method
of
gassing out
During a fermentation:
•
•
Stop supply of air
Linear decline in
DOC (zone AB) Start areation
(A)
•
again
(zone
BC)
Notes: Over the period, BC, the observed increase in dissolved oxygen concentration is the difference between the transfer of oxygen into solution and the uptake of oxygen by the respiring culture as expressed by the equation

## Slide 27
In Fig. 9.7 the slope of the line AB is a measure of the respiration rate of the culture.
At point B the aeration is resumed and the dissolved oxygen concentration increases until it reaches concentration X.
BC, the observed increase in dissolved oxygen concentration is the difference between the transfer of oxygen into solution and the uptake of oxygen by the respiring culture as expressed by the equation:
where x is the concentration of biomass
Qo2 is the specific respiration rate (mmoles of oxygen g -1 biomass h-1 ).
The term xQo2 is given by the slope of the line AB in Fig. 9.7.

## Slide 28
Dynamic Method of gassing out
This technique is convenient in that the equations may be applied using DOT rather than concentration because it is the rates of transfer and uptake that are being monitored so that the percentage saturation readings generated by the electrode may be used directly.
Notes: Thus, from equation (9.5), a plot of CL versus dCL/dt + xQo2 will yield a straight line, the slope of which will equal -1/KLa, as shown in Fig. 9.8.

## Slide 29
Factors affecting KLa value in fermentation vessels
The effect of air flow rate on KLa
Normally air flow rate used are 0.5 to 1.5 vvm
This air flow rate is maintained during scale up
If the impeller is unable to disperse the incoming air then OTR decreases extremely due to impeller flooding
Flooding is the phenomena where the air flow dominates the flow pattern
Notes: Vvm =vessel volume per minute
When implere is flooded, bubbles will accumulate underneath the impeller and coalesce (come together and form one mass or whole)

## Slide 30
Factors affecting KLa value in fermentation vessels
The effect of air flow rate on flow pattern
air-flow dominates flow pattern

## Slide 31
Factors affecting KLa value in fermentation vessels
The effect of Agitation degree on KLa

## Slide 32
Factors affecting KLa value in fermentation vessels
The effect of foam and antifoam on oxygen transfer
Presence of foam increases the residence time so air bubbles are depleted of oxygen
Foam in the impeller region prevents adequate mixing of
the fermentation broth
Antifoams are surfactants
- Collapse of bubbles in foam
- Decrease oxygen transfer rate
- Favours coalescence of bubbles (surface area increases)
Notes: Surfactants: lower the surface tension between two liquids

## Slide 33
Scale up
Two kinds of conditions must be satisfied to ensure similarity between the model and the prototype.
- similarity of the physical boundaries
- similarity of the flow fields
Study of problems associated with the transfer of experimental data from laboratory and pilot plant equipment to large scale industrial equipment
The fundamental requirement for scale up is that the model and the prototype should be the same to each other.

## Slide 35
Scale Up

## Slide 36
Physical boundaries
Preservation of geometric similarity of the physical boundaries
All linear dimensions of the model must be related to the corresponding dimensions of the prototype by diameter and height
i.e. Keep the ratio of the height H to diameter D t (tank) same in the model and prototype
Notes: - Ratio of surface to volume decreases during scale-up.

## Slide 37
- constant power input per volume(OTR)
- constant liquid circulation rate inside the reactor
- constant impeller tip speed (shear rate)
- constant Reynolds number( Heat transfer)
Dynamic similarity of the flow fields
To achieve dynamic similarity in a stirred-tank reactor, scale-up can be based on the following criteria in addition to geometric similar boundaries:
Notes: Shear rate is the rate of change of velocity at which one layer of fluid passes over an adjacent layer.

## Slide 38: Major factor in scale up
The cell/physiological state
The culture medium
Type of the bioreactor
Operational parameters

## Slide 39
Type of bioreactor
Stirred tank reactor
Air lift column
Bubble column

## Slide 40: Constant tip speed
N1= Impeller speed of small bioreactor
N2= Impeller speed of Large bioreactor
Di1= Impeller diameter of small bioreactor
Di2= Impeller diameter of large bioreactor
Notes: It affects the Shear rate which is : The rate of change of velocity at which one layer of fluid passes over an adjacent layer.

## Slide 41
N = Impeller speed
D = Impeller diameter
ρL= Density of the liquid
μL=Viscosity of the liquid
Constant Reynolds number
Notes: Reynold number: inertial force over viscous force

## Slide 42
Constant Power consumption per unit volume
Ungassed power consumption ,
Np
(Rushton’s equation)
Notes: N=rotational speed
Np= power number
Di= impller diameter
Po=ungassed power

## Slide 43
Constant Power consumption per unit volume
Ungassed power consumption ,
Gassed power consumption ,
(Rushton’s equation)
Notes: Pg=gassed power

## Slide 44
Constant Power consumption per unit volume

## Slide 45: Steps in scale up
Identification of the principal environmental domain affected by the aeration and agitation
Identification of the process variable which affects the identified environmental domain
Calculation of the value of the process variable to be used on the large scale

## Slide 46
Process Variable | Characteristics affected
Power consumption per unit volume | Oxygen Transfer Rate
Impeller tip speed | Shear Rate
Volumetric air flow rate | Oxygen Transfer Rate
Pumping rate | Mixing time
Reynolds number | Heat transfer