## Slide 1: Cadastral Surveying

## Slide 2: Basic Components of Cadastre
Land Registration
Private conveyancing, in which the records and transfers of land are handled by private arrangements; Registration of deeds, in which copies of such records are maintained by officials or by state
Property Taxation
Property tax is the most common local tax and that it necessitates efficient administration, which basically mean a well-established land and land related information system or cadastre. Thus, property taxation, especially in urban areas, is used as a major source of revenue.
Cadastral Surveying and Mapping
Cadastral surveying is a survey carried out for the purpose of providing information for the drawing of cadastral map.

## Slide 3: Parcel index map and parcel map
Parcel index map (PIM) – showing all parcels in particular jurisdiction. This map should reflect unique parcel identifiers which act as an index to various cadastral and land registrations attribute data.
Parcel map - showing details of dimensions (distance, azimuth) of the parcel boundaries the coordinates of the parcel corners, a short description of the monumentation of and other standard map data. This map serves us as a legal description for all registered parcels.

## Slide 4: The Cadastre and Land Tenure
Land tenure -- rights, restrictions, and responsibilities people have with respect to the land.
The most important types of land tenure or real property identified in most Cadastral systems can be characterized as follows:
Ownership: Exclusive right to use the parcel
Lease: right to use the parcel for limited time
Easement: owner of a parcel to use neighboring parcel
Mortgage: real property is pledged to secure money
Communal or group rights: family, community….
Other rights:

## Slide 5: Cadastral Database
Data that may appear in a cadastre include geometric data (coordinates, maps), property addresses, land use, real property information, the nature and duration of the tenure, details about the construction of buildings and apartments, population, and land taxation values.
The diversity of data brings the complexity in data management and requires to be managed by using an advanced database management system (DBMS).
A database may have special characteristics according to the structures of the data managed by, such as spatial databases which manage the geographical data.

## Slide 6: Cadastral survey
Cadastral surveys are surveys whose aim is to demarcate or create, measure, define/describe and record the position of boundary land as property.
Their ultimate purpose being to give unambiguous, graphical, numerical or descriptive information relating to location, extent, shape and size of land parcels. Such information is vital in the support of a register of titles for land ownership and transfer of rights in land.

## Slide 7: Demarcation:
is the process of physical marking (creating) boundaries on the ground to indicate the limits of a land parcel.
Boundary markers may also be required to be emplaced at all points where the boundary meets other features such as river, a shoreline, a road, a railway line, and other features which requires some kind of easement or right of way.

## Slide 8: Location of the parcel
The general location of a surveyed piece of land is carried in the heading of the survey job and should be written on the respective survey plan.
The heading describes the nature of the survey, giving the administrative name of the area where the land parcel situated.

## Slide 9: Extent, shape and size
the shape of a piece of land is given by the nature and extent of its boundaries in direction which are referenced to a particular orientation line.
In practice a coordinates system either local or national is established; and on it all surveys in a given area is related.
Together with the coordinates system reference line of orientations is established so that any point in the area can be uniquely described in terms of linear and angular measurements.
Distances, bearing, and areas are common information on cadastral plans.

## Slide 10: Boundary
A boundary is the extreme limit of something.
As for land parcel, a boundary may be defined as the line, alone or together with others, which encloses or defines the limits of the land parcel.
Such limits may be described in terms of numerical data, (such as bearings and distances or coordinate value), in which case this give rise to fixed boundaries

## Slide 11: General Boundaries
A general boundary is one whose position is not usually determined.
For this reason, such a boundary is said to be indeterminate or indefinite.
A boundary of this type may be marked by some physical feature such as stream, a wall and a hedge or its position may be described relative to features such as wall, a road, a stream etc. and the boundary may be unmarked.

## Slide 12: Fixed Boundary
This is a boundary line whose precise position has been created or determined and recorded by a survey operation.
Fixed boundaries make use of markers on the ground and are defined in accordance with specified accuracies that will enable parcels to be readily and reliably identified or relocated.
Such boundaries are usually linked to framework of geodetic horizontal control established over a country.
Because coordinates of the boundary markers are known, the name coordinated boundary is often used for fixed boundaries.

## Slide 13: The Role of Surveyors in Cadastre
a) Cadastral surveying
b) Survey recording
c) Land valuation
d) Land-use planning
e) Database management
f) Dispute resolution

## Slide 14: Cadastral Surveying Procedure
  Survey planning
  Hold a briefing for local residents
  Confirmation of boundary (parcel investigation)
  Survey the boundary after confirmation (Boundary Survey)
  Making cadastral record
  Confirming the results of Cadastral Survey
  Submit the product of Cadastral Survey to registry office

## Slide 15: The Surveying Process in Urban Areas
Data searching, pre-computations and initial job planning
Third Party Interest
Reconnaissance
Demarcations
Coordination
    Traverses
Computation
Detail Measurement

## Slide 16: Next time
---------->
---------->
Chapter 3
DATA CAPTURING TECHNIQUES