## Slide 1: CHAPTER THREE Vapor/liquid equilibrium
Nature of equilibrium
Gibbs Phase rule
Criteria of equilibrium
Clapeyron and Clausious claperon equation
Simple models for vapor/liquid equilibrium
VLE by modified raoult’s law
Flash calculation

## Slide 2: nature of equilibrium
Equilibrium is a static condition in which no changes occur in the macroscopic properties of a system with time.
Temperature
An isolated system Pressure remains fixed
Phase composition
Types of equilibrium
  Mechanical equilibrium – when =
  Thermal equilibrium – when = i.e. no heat flow.
  Material equilibrium – when = i.e. no flow of matter.
    Diffusion
    Phase change
    Chemical reaction
liquid
Vapor
Equilibrium is a static condition in which no changes occur in the macroscopic properties of a system with time.
Temperature
An isolated system Pressure remains fixed
Phase composition
Types of equilibrium
  Mechanical equilibrium – when =
  Thermal equilibrium – when = i.e. no heat flow.
  Material equilibrium – when = i.e. no flow of matter.
    Diffusion
    Phase change
    Chemical reaction

## Slide 3: Gibbs Phase rule
Gibbs phase rule: specifies the minimum number of independent variables needed to completely describe the system of interest and expressed in the form:
T,P, concentration
The number of independent intensive properties needed to fix the state of a system is called degrees of freedom (F).
Phase (P)
  a distinct, homogeneous state of matter
  Can be a mixture of components that cannot be distinguished from one another.
Component – an independently variable constituents of mixture.
where f is number of formulas,
e is number of chemical equilibrium equation,
i is number of initial condition.

## Slide 4: Gibbs Phase rule cond...
Example 3.1: Calculate degree of freedom or variance of each system.
  +
  @ 20ºC
  +
  in in
System | C=f-e-i |  |  |  | p | F=2+C-F | Variance
 | f | e | i | C |  |  | 
+ | 2 | 0 | 0 | 2 | 1 | 3 | T, P and
@ 20ºC | 3 | 1 | 0 | 2 | 2 | 2 | P
+ | 3 | 1 | 0 | 2 | 2 | 2 | T, P
in in | 3 | 0 | 0 | 3 | 2 | 3 | T, P and
System | C=f-e-i |  |  |  | p | F=2+C-F | Variance
 | f | e | i | C |  |  | 
 | 2 | 0 | 0 | 2 | 1 | 3 | 
 | 3 | 1 | 0 | 2 | 2 | 2 | P
 | 3 | 1 | 0 | 2 | 2 | 2 | T, P
 | 3 | 0 | 0 | 3 | 2 | 3 | 

## Slide 5: Gibbs Phase rule for one-component systems
Consider
F=2+C-P but C=1
F=3-P
Areas
P=1, therefore, F=2 which are T and P.
Curves
P=2, therefore, F=1 which is T or P.
Intersection/triple point
P=3, therefore, F=0

## Slide 6: Criteria of equilibrium for a closed system
For a closed system, the second law of thermodynamics states that:
TdS − dQ > 0 ………..(1)
From the first law of thermodynamics:
dU = dQ − PdV .…….(2)
Elimination of dQ between eqns (1) and (2) leads to:
TdS − dU − PdV 0 …….(3)
For constant internal energy and volume
≥0, When the system is at equilibrium, entropy reaches its maximum value.
= 0, @equilibrium
In differential form, Gibbs energy is given by
dG = d(H−TS) = d(U+PV−TS) dG=dU+PdV+VdP−TdS−SdT ……… (4)
dG + S dT − V dP 0 ................ (5)
≤ 0, When the system is at equilibrium, Gibbs energy reaches its minimum value.
= 0 , @equilibrium

## Slide 7: Clapeyron and Clapeyron-clausions Equation
Clapeyron equation: named after the French engineer and physicist E. Clapeyron (1799–1864), relates the enthalpy change associated with a phase change at constant T and P (such as the enthalpy of vaporization ) from knowledge of P, v, and T data alone.
Clapeyron–Clausius equation is used to determine the variation of saturation pressure with temperature.
We can derive C-C equation from Maxwell eqn and also from Gibbs function.
Clapeyron equation ……………..(6)
Clapeyron–Clausius equation ……………….(7)
(for vapor phase transition)

## Slide 8: Clapeyron Equation derivation
Consider the third Maxwell relation,
During a phase-change process, the pressure is the saturation pressure, which depends on the temperature only and is independent of the specific volume. Therefore:
For an isothermal - phase change process, the integration yields:
Read the derivation of Clapeyron equation from Gibbs function. (J. M. Smith page 207-208)

## Slide 9: Clapeyron-clausions Equation derivation
The Clapeyron equation can be simplified for liquid–vapor and solid–vapor phase changes by utilizing some approximations.
Assumption: - Ideal gas
- At low pressures
Substituting these approximations into Eqn (6), we find:

## Slide 10: Example 3.2:
The of ice at 273.15K is 6.01. The density of ice and liquid water are 920and 1000 respectively. Calculate the melting point of ice when the pressure is increased from 1.01*pa to 1.01*pa. (MW. of )
Given: 273.15K
1.01*pa = 6010
Required: ?
Solution:

## Slide 11: Example 3.3:
If the normal boiling point temperature of substance is 335K and its enthalpy of vaporization is 92.1:
  Calculate its boiling point temperature when pressure is increased 1atm to 5atm.
  What is the vapor pressure of the substance at 300K.
  Given:
  Required: a)
  b) @ ,
  Solution: a)
  b)

## Slide 12: Simple models for vapor/liquid equilibrium
When thermodynamics is applied to vapor-liquid equilibrium, the goal is to find by calculation the temperatures, pressures and compositions of phases in equilibrium.
Consider a mixture of 2 miscible components A and B:
vapor pressure
pure component A
MIX
vapor pressure
pure component B

## Slide 13: Raoult’s law
The two major assumptions required to reduce VLE calculations to Raoult's law are: - The vapor phase is an ideal gas - The liquid phase is an ideal solution
The mathematical expression which reflects the two listed assumptions and which therefore gives quantitative expression to Raoult's law is:
(i=1,2,…..,N) ……………………..(8)
where is a liquid-phase mole fraction,
is a vapor-phase mole fraction, and
is the vapor pressure of pure species i at the temperature of the system.
The product on the left side of Eq. (8) is known as the partial pressure of species i.

## Slide 14: Dewpoint and Bubble point
Vapor pressure - Composition diagram (where B is the more volatile component)
Bubble point
is the first trace of vapor.
Dewpoint
is the last trace of liquid.
Liquid
Vapor
Liquid + Vapor
A
B
P(atm)
T=constant
Moles %A Moles %B
BUBL P
Dew P

## Slide 15: Dewpoint and Bubble point Calculations with Raoult's Law
On dewpoint and bubble point calculations; there are four classes:
  BUBL P: calculate {and P, given {}and T
  DEW P: calculate { } and P, given {} and T
  BUBL T: calculate {}and T, given {}and P
  DEW T: calculate {}and T, given {}and P
Raoult’s Law: ……………………(8)
Antoni Equation:
………………….….(9)

## Slide 16: BUBL and dew point calculation

## Slide 17: BUBL and DEW p
Bubl P calculation:
Given: {}and T, Required: {and P.
Steps to calculate BUBL P:
Calculate vapor pressures of pure components using equation (9).
Calculate the bubble point pressure using:
………………(11)
Determine the composition of the vapor phase using:
……………………….(12)
2. DEW P calculation:
Given: {} and T, Required: { } and P.
Steps to calculate DEW P:
Calculate vapor pressures of pure components using equation (9).
Calculate the dew point pressure using:
…………….(13)
3. Determine the composition of the liqid phase using:
…………………(14)

## Slide 18: BUBL t calculation:
Given: {}and P, Required: {and T.
Algorism 1:
Assume
Using Antoni equation:
Assume @ j=0
Solve Eq. (15) to get for all i.
………..(15)
Solve Eq, (16) to get
…………..(16)
Solve Eq. (17) to get
…………..(17)
7. Is , then the iteration will be stopped.

## Slide 19: Dew t calculation:
Given: {} and P, Required: {} and T.
Algorism 2:
Assume
Using Antoni equation:
Assume @ j=0
Solve Eq. (18) to get for all i.
………..(18)
Solve Eq, (19) to get
…………..(19)
Solve Eq. (20) to get
…………..(20)
Is , then the iteration will be stopped.

## Slide 20: Example 3.4
Assuming Raoult's law to apply to the system Acetone(1), Acetonitrile(2) and Methyl acetate(3). Find T and {at given P=80kPa, and . Table 10.2 lists parameter values for the Antoine equation.
Given: P=80kPa,
and .
Required: T and {
Solution: Algorism 1
T= 332.77K
, and

## Slide 21: VLE by modified raoult’s law
For low to moderate pressures a much more realistic equation for VLE results when the second major Raoult's-law assumptions abandoned, and account is taken of deviations from solution ideality in the liquid phase by a factor inserted into Raoult's law, modified to read:
…………………....(21)
The factor is called an activity coefficient which are functions of temperature and liquid-phase composition.
Example 10.3 (J. M. Smith page 336)

## Slide 22: Flash calculation
An important application of VLE is flash calculation. The name originates from the fact that a liquid at a pressure equal to or greater than its bubble point pressure "flashes“ or partially evaporates when the pressure is reduced, producing a two-phase system of vapor and liquid in equilibrium.
The overall and component material balances around
the flash drum are given as: