## Slide 1
Engineering Geology CEng2132

## Slide 2: Course outline
Chapter 1:- Introduction
  Formation of the Earth and its parts
  Definition of geology
  Branches of geology
  Role of geology in civil engineering
Chapter2 :- Rocks and Minerals
  Formation of rocks
  Type of rocks and their classifications
  Minerals and their types

## Slide 3: Cont’
Chapter 3:- Geologic Structures
  Type of geologic Structures
  Formation of geologic Structures
  Effect of geologic Structures on civil stuctures
Chapter 4:- Geologic Surface Processes
  Weathering
  Movement of Slopes
  Wind Action and Desert Landscapes

## Slide 4: Cont’
Chapter 5:- Earth Quake
Chapter 6:- Geological Site Investigation
  Methods of investigation
  Geology of dam site
  Geology of reservoir site
  Geology of tunnel site
  Geology of road and bridge site
  Geology of building

## Slide 5: Chapter one Introduction
Formation of the planets and Earth

## Slide 6: Nebulae: step 1
Gas (98%) and dust (2%)
Rotates and is held together by gravitational force

## Slide 7: Step 2: The Nebula collapses
The collapsed mass forms a proto-sun due to gravitational force
Contraction increases speed of rotation: collapse

## Slide 8: Step 3: sun is formed, disk cleared
The disk is “cleared out” due to the immense amount of energy released.
Sun is formed
Dust and gases cool and condense in defined orbits around the sun

## Slide 9: Nebula hypothesis: step 4- planet formation
Temperature differences with respect to distance from sun
Closer, where temperatures are higher, iron and silicates condense
Farther, cooler, hydrogen, water condense
material collides and accretes forming planetesimals (small planets)

## Slide 10: This interaction between the earth’s magnetosphere and the solar wind. Early in the Earth’s formation the solar wind blew the light gases, H an He to the farther reaches of the solar system.

## Slide 11: Fig. 6.9
Schematic diagram illustrating Elsassar’s model for the Earth’s magnetic field. The solid mantle rotates at a different rate from the liquid outer core, which is molten Fe and Ni sulfides.
The magnetic field is important for the evolution of complex life on Earth since it shields organisms from cosmic radiation (the same high-energy particles that form C-14 in the upper atmosphere.

## Slide 12: Stages in Formation of Early Earth

## Slide 13
Early Earth (4.6 b.y.) had uniform composition and density
Heat generated by gravitational contraction, collisions with debris in its orbital path and decay of radioactive elements results in (partial) melting;
during molten phase dense elements (Fe and Ni) sink to collect in core and lighter silicate minerals flow upward to form mantle and crust
• Differentiation results in layered planet, and emission of gases supplies material for early atmosphere and oceans

## Slide 16: Divisions of the Earth's interior
Cross section of Earth showing in a rudimentary way the relation of the upper mantle to subduction zones and midocean ridges.
Note also the region where basaltic magma is thought to form.

## Slide 17
Geology
  is the study of the earth
  Deals with composition , structure & history of the earth
Two broad areas:
  Historical Geology – origins and evolution of the Earth, its continents, atmosphere and life
  Physical Geology – rocks, minerals and the processes that affect them

## Slide 18: sub-disciplines of geology
Geochemistry
  Deals with chemical composition of the earth

## Slide 19: Cont’
Geophysics
We can measure the physical properties of rocks that can be used to investigate the subsurface properties of the planet with a variety of methods
  Seismic
  Gravity
  Electromagnetic

## Slide 20: Cont’
Paleontology
  Deals with ancient fosils

## Slide 21: Cont’
Economic Geology
  Deals with geologic resources having economic value

## Slide 22: Cont’
Environmental geology
Deals with Geological, climatic and man-made hazards

## Slide 23: Cont’
Volcanology
  Monitor active volcanoes
  Predict eruptions

## Slide 24
Engineering geology
  application of Geology to engineering practice
  the application of geological data, techniques and principles

## Slide 25
  To the study of rock and soil material and ground water.
    essential for the proper location, planning, design, construction, operation and maintenance of engineering structures

## Slide 27: St. Francis Dam near Los Angeles St. Francis Dam near Los Angeles

## Slide 28: St. Francis Dam After failure

## Slide 29: Geological section of St. Francis Dam

## Slide 30: Main reasons for dam failure:
Sedimentary rocks on the west lost strength when it is wet;
The fault separating the west and east rock formations started to leak water;
Schist on the east increases pore pressure and lost shear strength after wet.

## Slide 31: Chapter2 Rocks and Minerals
Element mineral Rocks
In engineering Rock are significant for two major reasons :
  As building materials for constructions;
    Strength
    Durability
  As foundations on which the constructions are setting
    Density
    Strength
    Compressibility

## Slide 33: Bonding for stability
atoms share and transfer electrons In order to fill shells and reach a stable state
They bond in four different ways to do this
Ionic Bonding: (“electron transfer”) One atom donates one or more electrons to an atom of another element. Ex: NaCl

## Slide 34: Covalent Bonding
Highest energy level shell has 4 electrons but needs 8 for stability
Each C atom shares two electrons with four other C atoms

## Slide 35: Van der Waals Bonding
This is a weak bond formed from the secondary attraction of molecules as a result of the transfer or sharing of electrons

## Slide 36: Metallic Bonding
This form of bonding is unique to metals
Electrons in the outer shells are shared between several atoms
Makes them good conductors of heat and electricity

## Slide 37: What is a mineral? `
a naturally occurring chemical element or compound;
formed by inorganic processes;
solid
with an ordered arrangement or pattern for its atoms –crystalline structure;
possesses a definite chemical composition or range of compositions.

## Slide 38
So we can simply express the mineral as mineral = composition + crystalline structure
For two minerals if the composition are the same but the structures are different, they can be called a pair of polymorphs.
diamond/graphite (C, the same composition of carbon but different structure);

## Slide 40
From an engineering point of view, special concern of certain minerals are essential especially when they are introduced into or encountered with another mineral
gypsum in a limestone can become swelling when water presents;
pyrite (the fool’s gold) in shale can be deteriorated by acid water;
swelling clays in shale can become wetting and cause instability problem of a slope.

## Slide 42: Mineral Identification
Color
Flourite
Flourite

## Slide 43
Streak
The streakof a mineral is the color of the powder left on a streak plate

## Slide 44
Luster
  Luster refers to how light is reflected from the surface of a mineral
  Metallic and
  nonmetallic
Quartz
greasy
Rosequartz
vitreous

## Slide 45
Hardness
•The hardness of a mineral is its “scratchability”,
  determined by Moh’shardness scale.
  The hardest mineral known, diamond, was assigned the number 10.

## Slide 47
Specific Gravity
  is the "heaviness" of a mineral.
  It is the ratio of the weight of a mineral and the weight of an equal volume of water.
Common rock-forming minerals (quartz, feldspar, calcite, etc.) have specific gravity near 2.7

## Slide 48
Cleavage
Cleavage is the ability of a mineral to break along preferred planes

## Slide 49
Crystal forms
are displays of well-formed crystal faces by a mineral
Beryl -hexagonal
Diamond-octahedron

## Slide 50
Thousands of mineral species have been identified
• Only ~20 make up the earth’s crust
12 elements make up 99% of the earth’s crust.

## Slide 51
What is a ‘rock’?
In Geology
Rock is defined as the solid material forming the outer rocky shell or crust of the earth
In Engineering
Rock is the hard and durable material.

## Slide 52: Types of Rock
According to their origin, rocks are divided into three groups,
  the igneous,
  metamorphic and
  sedimentary rocks.

## Slide 53: Igneous Rocks
Igneous rocks are formed when hot molten rock material called magma solidifies.
Magmas are developed when melting occurs either within or beneath the Earth’s crust, that is, in the upper mantle.
They comprise hot solutions of several liquid phases, the most conspicuous of which is a complex silicate phase.
Thus, igneous rocks are composed principally of silicate minerals.

## Slide 54
Igneous rocks are divided into intrusive and extrusive types, according to their mode of occurrence.
intrusive:- the magma crystallizes within the Earth’s crust
extrusive:- solidifies at the surface, having erupted as lavas and/or pyroclasts from a volcano.
The intrusions have been exposed at the surface by erosion.

## Slide 55: The Identification Chart of the Igneous Rocks

## Slide 56: Engineering Aspects of Igneous
The plutonic igneous rocks are characterized by granular texture, massive structure and relatively homogeneous composition.
In their unaltered state, they are essentially sound and durable with adequate strength for any engineering requirement

## Slide 57
intrusive rocks may be highly altered by weathering or hydrothermal attack; furthermore, fissure zones are common.
The rock mass may be fragmented along such zones
Igneous rocks are good for dimension stone (tombstone etc.) because their resistance to weathering but need avoid fractures

## Slide 58: Sedimentary rocks
Sedimentary rocks are lithified sediments that held together by various types of cementing agents, such as
  calcite,
  quarts, and
  iron oxide; or
  by compaction of the mineral grains into an indurate mass.

## Slide 59: Types of Sedimentary rocks
Limestone is produced from the mineral calcite (calcium carbonate) and sediment.
  The main source of limestone is the limy ooze formed in the ocean.

## Slide 60
Sandstone is a sedimentary rock that formd from the cementing together of sand sized grains forming a solid rock.
Quartz is the most abundant mineral that forms sandstone.
Calcium carbonate, silica, or iron has been added to the water that is in contact with the sand grains.

## Slide 61
Chert is a very hard sedimentary rock that is usually found in nodules in limestone.
It probably formed from the remains of ancient sea sponges or other ocean animals that have been fossilized.
Silica has replaced the tissue forming the sedimentary rock.

## Slide 62
Conglomerate is a sedimentary rock that forms from the cementing of rounded cobble and pebble sized rock fragments.
Conglomerate is formed by river movement or ocean wave action.
The cementing agents that fill the spaces to form the solid rock are silica, calcite, or iron oxides.

## Slide 63: Engineering Aspects of Sedimentary rocks
The main problem of sand stone are
  Low strength
  Durability
  High permeability and porosity
Limestone develop caves

## Slide 64: Metamorphic Rocks
Metamorphic rocks are derived from pre-existing rock types and have undergone mineralogical, textural and structural changes.
The changing conditions of temperature and/or pressure are the primary agents causing metamorphic reactions in rocks.

## Slide 65: Metamorphic Structure
Foliation : Laminated structure resulting from segregation of different minerals into layers
Schistosity : the Varity of foliation that occur in the coarse grained metamorphic rocks.
  It results from of parallel arrangement of platy and ellipsoidal mineral grains.
Gneissosity : band of coarse grained mineral

## Slide 66: Types of Metamorphic Rocks
Slate & Mica schist : from mudstone (shale)
Green schist : from basalt and gabbro
Quartzite :Qtz arenite
Marble : limestone

## Slide 67: Engineering Aspects of metamorphic rocks
For metamorphic rocks the stability of rock mass greatly affected by the foliation orientation;
Marble as a metamorphic rock from carbonate sedimentary rocks can cause similar problems, eg., leakage of reservoirs, solution cavities, and channels.

## Slide 68: Rock Cycles

## Slide 69: Chapter Three Geologic Structures
The rocks of the earth’s crust are subjected to a number of forces
undergo deformation to varying degrees
depending upon
  the intencity
  type of the forces, and
  rigidity of the rocks.

## Slide 70
If stress is not equal from all directions (differential stress)
Tensional stress (or extensional stress), which stretches rock;
Compressional stress, which squeezes rock; and
Shear stress, which result in slippage and translation.

## Slide 72: Folds
when one or a stack of originally flat and planar surfaces, such as sedimentary strata, are bent or curved as a result of permanent deformation

## Slide 74
Parts of fold divided into
  hinge: where the flanks join together
  Limb: flanks of the fold

## Slide 75: Types folds
anticlines : beds are bent upwards
  fold will be convex upwards
  younger beds occur towards convex side
Synclines: beds are bent downwards
  fold will be convex downwards
  younger beds occur towards the concave side.

## Slide 78: Effects of folding:

## Slide 80: Fault
a planar fracture or discontinuity in a volume of rock, across which there has been significant displacement along the fractures

## Slide 82: Types of faults
Translational fault

## Slide 83: Normal fault

## Slide 84: Reverse fault

## Slide 85: Effect of faults
Collapsed Structure, Oakland, California
Faults generate earthquakes
Bound the tectonic plates of the Earth
Deform the Earth’s surface
Fluid transport in the Earth's crus
  Water
  Magma
  Hydrocarbons
  Hydrothermal fluids
Faults are zones of weakness to account for in engineering projects

## Slide 87: Joints
fracture in rock where the displacement associated with the opening of the fracture is greater than the displacement due to lateral movement in the plane of the fracture (up, down or sideways) of one side relative to the other
  little to no lateral movement across joints
  normally have a regular spacing
  generally occur as sets

## Slide 90: Effects of joints
reduce the competence of rock mass
increase the porosity and permeability
make them susceptible to quick decay and weathering
avenues for the leakage of water in case of reservoirs
pose ground water problems in tunnelling
increases the ground water potentiality facilitate the quarrying process or tunnelling process
also reduce the cost by decreasing the use of explosives

## Slide 91: Chapter Four Geologic Surface Processes
WEATHERING
  slowly break down of rocks when exposed to atmospheric conditions
Two types
Mechanical Weathering
Chemical Weathering

## Slide 92: Mechanical Weathering
disintegration of rocks into smaller pieces by exfoliation or decrepitation (slaking)
The chemical composition of the parent rock is not altered

## Slide 93: Agents of mechanical weathering
frost action,
salt crystallization,
temperature changes (freezing and thawing),
moisture changes (cycles of wetting and drying),
wind,

## Slide 94
glaciers,
streams,
unloading of rock masses (sheet jointing), and
biogenic processes (plants, animals, etc.).

## Slide 95: Chemical Weathering
weathering creates new minerals in place of the ones
most important atmospheric reactants are
  oxygen,
  carbon dioxide, and
  water

## Slide 96
Solution is a reaction whereby a mineral completely dissolves during weathering
  evaporite minerals (salt, gypsum) dissolve quickly in water
  Limestone dissolves by meteoric water
    formation of cavities called dolines or karsts
    sink holes

## Slide 97
Hydrolysis : reaction between acidic weathering solutions and many of the silicate minerals
  Feldspars are transformed by hydrolysis to clay minerals
Hydration : the penetration of water into the lattice structure of minerals
  anhydrite into gypsum
Oxidation : the reaction of free oxygen with metallic elements
  iron atoms contained in the minerals lose one or more electrons each and then precipitate as different minerals
  transformation of pyrite (FeS2) into iron hydroxides

## Slide 98: Effect of Weathering in Engineering
increase porosity, permeability and deformability
Decreases strength
controls the depth to the bedrock and the uniformity of this contact.
geologic hazards
  block movement
  landslides

## Slide 99: Chapter Five Earth Quake

## Slide 100: Chapter Six Geological Site Investigation
general objective of a site investigation is to assess the suitability of a site for the proposed purpose
involves exploring the ground conditions at and below the surface
a prerequisite for the successful and economic design of engineering structures and earthworks
usually consists of three stages

## Slide 101: Desk Study
to ascertain a general picture of the existing geological conditions prior to a field investigation.
save time
reduce the cost of the site investigation
prevent duplication of effort.

## Slide 102: Preliminary Reconnaissance
a walk over the site
To check a conclusions reached in the desk study.
note
  distribution of the soil and rock types present,
  the relief of the ground,
  the surface drainage and associated features,
  any actual or likely landslip areas
  , ground cover and obstructions,
  earlier uses of the site such as tipping or evidence of underground workings

## Slide 103: Site Exploration
Detailed investigation of the site
  Direct Methods : to obtain surfface information of the site
  Indirect Methods (Geophysical Methods) : to provide subsurface information over a large area at reasonable cost.
    to determine the geological sequence and structure of subsurface rocks by the measurement of certain physical properties or forces

## Slide 104
seismic and resistivity methods record the artificial fields of force applied to the area under investigation
magnetic and gravitational methods measure natural fields of force

## Slide 105: Geology of Dam Sites
Geologic factor
  control the character of the foundation
  govern the materials available for construction
The major questions that need answering
  the depth at which adequate foundations exist,
  the strengths of the rock masses involved,
  the likelihood of water loss and
  any special features that have a bearing on excavation

## Slide 106
dam sites located in sandstones are normally transected by joints
  reduce resistance to sliding.
thin-bedded, highly folded or cavernous limestone are likely to present serious foundation or abutment problems
  bearing capacity or
  water tightness
Beds separated by layers of clay or shale, especially those inclined downstream, may serve as sliding planes

## Slide 107
Fresh metamorphosed rocks such as quartzite and hornfels are very strong and afford excellent dam sites
Cleavage, schistosity and, foliation adversely affect their strength and make them more susceptible to decay
Joints and shear zones are responsible for the unsounding of rock

## Slide 108: Geology of Tunnel
Geology is the most important factor that determines the
  nature,
  form and
  cost of a tunnel
tunnel stability in areas of karstic limestone associated with
  weathered rock,
  abrupt changes in lithology,
  rock weakened by dissolution or
  containing discontinuites opened by dissolution,.

## Slide 109
Construction of a tunnel may alter the groundwater regime of the locality
  dewatering, leading to sinkhole development
    surface subsidence

## Slide 110: Geology of Highways and bridge
construction of a highway requires the excavation of soils and rocks, and stable foundations for the highway, as well as construction materials
The ground beneath roads and, more particularly, embankments,
  must have sufficient bearing capacity to prevent foundation failure and
  capable of preventing excess settlements due to the imposed load

## Slide 111: Geology of Buildings site
Footings distribute the load to the ground over an area sufficient to suit the pressures to the properties of the soil or rock.
Their size of footing is governed by the strength of the foundation materials.
The amount and rate of settlement of a footing due to a given load is a function of
  the dimensions of the base
  the compressibility of the foundation materials

## Slide 112
gravels and dense sands afford good foundations
The position of the water table in relation to the foundation structure has an important influence on
  the ultimate bearing capacity.
High groundwater levels lower the effective stresses in the ground
  the ultimate bearing capacity is reduced

## Slide 113: Assignment
Why engineering geology is important in civil engineering ?
Briefly discus the rock cycle
If you provided with piece of igneous rock and asked you to identify it, how you identify into intrusive and which type of it or extrusive and which type.
Discuss briefly advantage and disadvantage of joints from engineering point of view