## Slide 1: Chapter: Six
Quality Control and Monitoring

## Slide 2: Quality Control
Clause 33: Identifying Defects
  The Engineer shall check the Contractor’s work and notify the Contractor of any Defects that are found. Such checking shall not affect the Contractor’s responsibilities
Clause 34: Tests
  If the Engineer instructs the Contractor to carry out a test not specified in the Specification to check whether any work has a Defect and the test shows that it does, the Contractor shall pay for the test and any samples. If there is no Defect, the test shall be a Compensation Event.

## Slide 3: …Continued
Clause 35:Correction of Defects
  The Engineer shall give notice to the Contractor of any Defects before the end of the Defects Liability Period, which begins at Completion, and is defined in the Special Conditions of Contract
  Every time notice of a Defect is given, the Contractor shall correct the notified Defect within the length of time specified by the Engineer’s notice.
  The Defects Liability Period shall be extended for as long as Defects remain to be corrected.
Clause 36: Un corrected defects
  If the Contractor has not corrected a Defect within the time specified in the Engineer’s notice, the Engineer will assess the cost of having the Defect corrected, and the Contractor will pay this amount.

## Slide 4: Quality control
EBCS2-1995, 9.4 measures to be taken in case of non-compliance
If the quality of the structure is found to be in doubt after an inspection or from the test results, then a special examination shall be made to verify the soundness of the information received and to asses the actual strength of the structure constructed with possible recourse to more accurate methods of calculations.
Sequence of measures
The following sequential measures shall be taken where the results of compliance control tests or inspection are unsatisfactory:
The position of concrete which does not fulfill the compliance criterion shall be identified
The structural safety shall be checked by appropriate calculations on the basis of the actual tests which did not comply. If safety is assured, the concrete can be accepted.
If the structural safety or durability are not assured, then the strength of the concrete shall be examined by taking drilled cores or by non-destructive methods. The results of the tests shall be assessed on the basis of the prescribed acceptance criterion, taking into account any differences in age.

## Slide 5: …Continued
If this new information's shows that structural safety is assured, the concrete may be accepted after it has been decided whether repairs are necessary to ensure durability
If the results of check tests by non-destructive methods show that the quality of concrete is inadequate or show other defects, the engineer may require a loading test to be made which shall then carried out in accordance with procedure set in 9.4.4
If the structural safety and durability are not assured, then the possibility of strengthening the structure must be investigated. If strengthening is not feasible, then the concrete shall be rejected, and the structure or member demolished or given a reduced structural grading by limiting its service rating, as appropriate.

## Slide 6: Thank You!!!